## Slide 1: Programmed I/O, Interrupts, and DMA

## Slide 2: Programmed I/O, Interrupts, and DMA
Input/Output Characteristics
  Many orders of magnitude slower than memory
  Character vs. block based
  Burst vs. steady transfers
  Three approaches to I/O
    Programmed
    Interrupt-driven
    Direct memory access

## Slide 3: Programmed I/O, Interrupts, and DMA
Programmed I/O
  CPU is responsible for reading/writing to devices
    Special “input” instruction on CPU
    I/O data register and I/O address register
    Each device is assigned a unique address.
Englander, 2009, p. 283

## Slide 4: Programmed I/O, Interrupts, and DMA
Programmed I/O
  Memory mapped I/O alternative
    Treat the I/O device as a memory address for reads and writes. Simplifies programmer interface; slightly more complicated control circuitry.
  Problems with all programmed I/O
    Must check status bits to see if I/O is “ready.”
    Use a polling loop (busy-wait) to send and receive data to devices.

## Slide 5: Programmed I/O, Interrupts, and DMA
Programmed I/O
  Memory mapped I/O alternative
    Treat the I/O device as a memory address for reads and writes. Simplifies programmer interface; slightly more complicated control circuitry.
  Problems with all programmed I/O
    Must check status bits to see if I/O is “ready.”
    Use a polling loop (busy-wait) to send and receive data to devices.
SET kbdStatus, r1 ; addr of status
wait: LOAD [r1], r2 ; load status data
AND r2, 1, r2 ; check ready flag
BRZ wait ;
SET kbdBuff, r1 ; addr of data
LOAD [r1], r2 ; r2 has keypress

## Slide 6: Programmed I/O, Interrupts, and DMA
Interrupts
  Busy-waits (polling) wastes resources but has simpler hardware.
  Alternative: After an I/O request from the CPU, let the I/O device notify the CPU when data is ready to be read (called an interrupt).
    Each device is assigned an IRQ line (signal).
    I/O controller sets IRQ line status high.
    CPU detects IRQ at beginning of fetch/execute.
    CPU saves state of running program and switches to an IRQ handler routine.
    Routine services the request.
    Control is returned to the previously running code.

## Slide 7: Programmed I/O, Interrupts, and DMA
Interrupts
  Changes to fetch/execute cycle

## Slide 8: Programmed I/O, Interrupts, and DMA
Interrupts
  Changes to fetch/execute cycle
Issues:
Additional control hardware
Queuing of interrupts
Masking interrupts
Registering handlers (part of the OS)

## Slide 9: Programmed I/O, Interrupts, and DMA
Interrupts
Problems with interrupt driven I/O
  CPU still involved with each interrupt
  Only transfers a single byte/word

## Slide 10: Programmed I/O, Interrupts, and DMA
Interrupts
  Problems with interrupt driven I/O
    CPU still involved with each interrupt
    Only transfers a single byte/word
Disk or network transfers may be hundreds or thousands of bytes. IRQ handler code may be hundreds of instructions. Still too much overhead.

## Slide 11: Programmed I/O, Interrupts, and DMA
DMA
  Direct Memory Access (DMA)
    Add a specialized kind of CPU that can directly transfer data from device to memory.

## Slide 12: Programmed I/O, Interrupts, and DMA
DMA
  Direct Memory Access (DMA)
    Add a specialized kind of CPU that can directly transfer data from device to memory.

## Slide 13: Programmed I/O, Interrupts, and DMA
DMA
  Direct Memory Access (DMA)
    Add a specialized kind of CPU that can directly transfer data from device to memory.
CPU uses PIO to specify memory address, operation (read/write), byte count, and block location on disk.

## Slide 14: Programmed I/O, Interrupts, and DMA
DMA
  Direct Memory Access (DMA)
    Add a specialized kind of CPU that can directly transfer data from device to memory.
DMA controller initiates I/O with the device controller.

## Slide 15: Programmed I/O, Interrupts, and DMA
DMA
  Direct Memory Access (DMA)
    Add a specialized kind of CPU that can directly transfer data from device to memory.
DMA controller receives data and transfers it to memory.

## Slide 16: Programmed I/O, Interrupts, and DMA
DMA
  Direct Memory Access (DMA)
    Add a specialized kind of CPU that can directly transfer data from device to memory.
DMA controller interrupts CPU to notify data transfer is complete.

## Slide 17: Programmed I/O, Interrupts, and DMA
DMA
  Direct Memory Access (DMA)
    Add a specialized kind of CPU that can directly transfer data from device to memory.
CPU handles interrupt. All bytes are in memory for processing.

## Slide 18: Programmed I/O, Interrupts, and DMA
DMA
  Direct Memory Access (DMA)
    Add a specialized kind of CPU that can directly transfer data from device to memory.

## Slide 19: Programmed I/O, Interrupts, and DMA
Summary
  Purely programmed I/O requires special I/O instructions, I/O data and address registers, and polling loops that waste CPU resources.
  Interrupt-driven I/O avoids busy-waiting but is unsuitable for large block transfers due to interrupt handler execution overhead.
  DMA combines PIO and IRQ handlers with a special controller to transfer large amounts of block data efficiently directly to memory.

## Slide 20: References
  Englander, I. (2009). The architecture of computer hardware and systems software: an information technology approach. Wiley.