## Slide 1: Chapter 1
Data Communications and
Network Management Overview

## Slide 2: Telephone Network
• Modern network evolution from Telephone /Telecommunications Network
• Characteristics of Telephone network
• Reliable - does what is expected of it
• Dependable - always there when you need it (remember 911?)
• Good quality (connection) - hearing each other well
• Reasons for QoS:
• Good planning, design, and implementation
• Good operation and management of network
• Migration to new technologies –
• e.g., From analog to digital technology

## Slide 3: Telephone Network Model
Notes
• Notice the hierarchy of switches
• Primary and secondary routes
programmed
• Automatic routing
• Where is the most likely failure?
• Use of Operations Systems to ensure QoS

## Slide 4: OSSs / NOC
• Operations Support Systems (OSSs) help
manage the operation of networks
• OSSs in telecommunications monitor:
• Analog network parameters:
•S/N ratio, transmission loss, call blockage, etc.
• Digital network parameters:
• Packet loss, Packet delay, Throughput, QoS, etc.
• Real-time management of network.
• Trunk (logical entity between switches / nodes) maintenance system measures loss and S/N Trunks not meeting QoS removed before
customer notices poor quality.
• Traffic measurement systems measure call drops and blockage. Additional switches or routers planned to keep the call blockage or drops below acceptable level.
• OSSs distributed at central offices and customer premises
• Network management done centrally from Network Operations Center (NOC).

## Slide 5: Data and Telecommunication Network

## Slide 6: Notes: • Computer data is carried over long distance by telephone (telecommunication network). • Output of telephone is analog and output of computers is digital. • Modem is used to “modulate” and “demodulate” computer data to analog format and back. • Clear distinction between the two networks is getting fuzzier with modern multimedia networks
Data and Telecommunication Network- cont.

## Slide 7: Migration to Digital Technology

## Slide 8: Notes: • Analog transmission migrated to digital transmission. • Analog sources converted to digital signals. • CPE (Customer Premises equipment) included digital PBX (Private Branch Exchanges). • Analog bandwidth hierarchy migrated to synchronous digital hierarchy.
Migration to Digital Technology- cont.

## Slide 9: DCE with LAN DCE.. Distributed Computing Environment
Notes:
DCE.. Distributed Computing Environment
• Driving technologies for
DCE:
• Desktop processor
• LAN
• LAN - WAN network

## Slide 10: LAN-WAN Network
Notes:
• Major impacts of DCE:
• No more monopolistic service provider.
• No centralized IT controller.
• Hosts doing specialized function.
• Client/Server architecture formed the Core of DCE network.

## Slide 11: Client/Server Model
Notes:
• Post office analogy; clerk the server, and the customer the client.
• Client always initiates requests.
• Server always responds.
• Notice that control is handed over to the receiving entity.

## Slide 12: Client/Server Examples

## Slide 13: • TCP/IP is a suite of protocols. • Internet is based on TCP/IP. • IP is Internet protocol at the network layer level. • TCP is connection-oriented transport protocol and ensures end-to-end connection. • UDP is connectionless transport protocol and provides datagram service. • Internet email and much of the network mgmt. messages are based on UDP/IP. • ICMP part of TCP/IP suite.
TCP/IP Based Networks

## Slide 14: TCP/IP Based Networks
• TCP/IP is a suite of protocols
• Internet is based on TCP/IP
• IP is Internet protocol at the network layer level
• TCP is connection-oriented transport protocol and ensures end-to-end connection
• UDP is connectionless transport protocol and provides datagram service
• Internet email and much of the network mgmt. messages are based on UDP/IP
• ICMP part of TCP/IP suite

## Slide 15: Internet Configuration
Notes:
• Walk through the scenario of email from Joe to Sally.

## Slide 16: Architecture, Protocols and Standards
• Communication architecture
• Modeling of communication systems, comprising
• Functional components
• Operations interfaces between them
• Communication protocols
• Operational procedures
• Intra- and inter-modules
• Communication standards
• Agreement between manufacturers on protocols of communication equipment on
• Physical characteristics
• Operational procedures
Notes:
• Examples: (Students to call out)

## Slide 17: Communication Architecture
Notes:
• Inter-layer interface: user and service provider.
• Peer-layer protocol interface.
• Analogy of hearing-impaired student.
• Role of intermediate systems.
• Gateway: Router with protocol conversion as gateway to an autonomous network or subnet.

## Slide 18: OSI Reference Model
Notes:
• Importance of the knowledge of layer
Structure in NM.

## Slide 19: OSI Layers and Services
Notes
• Importance of services offered by different layers and the protocol conversion at different layers in NM

## Slide 20: PDU Communication Model
Notes:
• What is the relevance of PDU model in NM?

## Slide 21: Gateway
Notes:
• cc:mail from a station in Novel IPX network to an Internet station with SMTP email

## Slide 22: OSI and Internet
Notes:
• Simplicity of Internet; specifies only layers 3 and 4
• Integrated application layers over Internet
• Commonality of layers 1 and 2 - IEEE standard

## Slide 23
Application Protocols

## Slide 24: Application Protocols-cont.
Internet user | OSI user
Telnet | Virtual Terminal
File Transfer Protocol | File Transfer Access & Mgmt
Simple Mail Transfer Protocol | Message-oriented Text Interchange Standard
Simple Network Management Protocol | Common Management Information Protocol
Notes:

## Slide 25: Broadband Network

## Slide 26
Broadband Access Networks

## Slide 27: Centrally Managed Network Issues

## Slide 28: • Loss of connectivity • Duplicate IP address • Intermittent problems • Network configuration issues • Non-problems • Performance problems
Some Common Network Problems:

## Slide 29: • Reliability • Non-real time problems • Rapid technological advance • Managing client/server environment • Scalability • Troubleshooting tools and systems • Trouble prediction • Standardization of operations - NMS helps • Centralized management vs. “sneaker-net”
Challenges of IT Managers:

## Slide 30: Network Management
Notes:
• OAMP
• Operations
• Administration
• Maintenance
• Provisioning

## Slide 31: NM Functional Flow Chart

## Slide 32: Dumbbell Architecture
Notes:
• Message exchange between NMSs managing different domains

## Slide 33
NM Components

## Slide 34: Interoperability
Notes:
• Message exchange between NMSs managing different domains.

## Slide 35: • Network Management • Service Management • Service and Network Provisioning • Application Management • e-Commerce Management • Inventory Management • Integrated Management • Business Management • Information Management • Management Protocols • Management Technologies
Network Management Perspectives

## Slide 36: • Domains • Protocols • Technologies • Transmission Media • Transmission Modes • Service Functions
Infrastructure Perspective:
Service Perspective:
• Communication Services
• Computing Services
• Content Services
• IT Services
• Application Services

## Slide 37: • Status: • SNMP management • Limited CMIP management • Operations systems • Polled systems • Current Focus: • Object-oriented approach • Service and policy management • Business management • Web-based client management • Future Trends • Web-based management? • XML based management
Status and Future Trends
Nisreen AlGhadban 120015789