## Slide 1: Chapter 5
SNMPv1 Network Management:
Communication and Functional Models

## Slide 2: SNMP Architecture
Notes:
Truly simple network management protocol
Five messages, 3 from manager and 2 from agent

## Slide 3: SNMP Messages
Get-Request
Get-Next-Request
Set-Request
Get-Response
Trap
  Generic trap
  Specific trap
  Time stamp
Notes :
Generic trap
  coldStart
  warmStart
  linkDown
  linkUp
  authenticationfailure
  egpNeighborLoss
  enterpriseSpecific
Specific trap
  For special measurements such as statistics
Time stamp: Time since last initialization

## Slide 4: Administrative Model
Based on community profile and policy
SNMP Entities:
  SNMP application entities - Reside in management stations and network elements - Manager and agent
  SNMP protocol entities - Communication processes (PDU handlers) - Peer processes that support application entities

## Slide 5: SNMP Community
Notes :
Security in SNMPv1 is community based
Authentication scheme in manager and agent
Community: Pairing of two application entities
Community name: String of octets
Two applications in the same community communicate with each other
Application could have multiple community names
Communication is not secured in SNMPv1 - no encryption

## Slide 6: Community Profile

## Slide 7: Community Profile- cont.
Notes :
MIB view
  An agent is programmed to view only a subset of managed objects of a network element
Access mode
  Each community name is assigned an access mode: read-only and read-write
Community profile: MIB view + SNMP access mode
Operations on an object determined by community profile and the access mode of the object
Total of four access privileges
Some objects, such as table and table entry are non-accessible

## Slide 8: Administrative Model
Administrative model is SNMP access policy
SNMP community paired with SNMP community profile is SNMP access policy
Notes :
Parameters:
Community / communities
Agent / Agents
Manager / Managers

## Slide 9: Access Policy
Notes :
Manager manages Community 1 and 2 network components via Agents 1 and 2
Agent 1 has only view of Community Profile 1,e.g., Cisco components
Agent 2 has only view of Community Profile 2,e.g., 3Com components
Manager has total view of both Cisco and 3Com components

## Slide 10: Generalized Administrative Model
Notes :
Manager 1 manages community 1, manager 2 community 2, and manager 3 (MoM) both communities 1 and 2

## Slide 11: Proxy Access Policy
Notes :
Proxy agent enables non-SNMP community elements to be managed by an SNMP manager.
An SNMP MIB is created to handle the non-SNMP objects.

## Slide 12: Protocol Entities
Notes :
Protocol entities support application entities
Communication between remote peer processes
Message consists of:
  Version identifier
  Community name
  Protocol Data Unit
Message encapsulated and transmitted

## Slide 13: Get and Set PDU
VarBindList: multiple instances of VarBind pairs
PDU Types: enumerated INTEGER
Notes :

## Slide 14: Error in Response
Error Index: No. of VarBind that the first error occurred

## Slide 15: Trap PDU
Figure 5.8 Get and Set Type PDUs
Table 5.1 Generic Traps

## Slide 16: Trap PDU-cont.
Notes :
Enterprise and agent address pertain to the system generating the trap
Seven generic traps specified by enumerated INTEGER
Specific trap is a trap not covered by enterprise specific trap
Timestamp indicates elapsed time since last re-initialization

## Slide 17: SNMP Operations

## Slide 18: MIB for Get-Next-Request

## Slide 19: Lexicographic Order
Table 5.2 Lexicographic-Order Number Example
Notes :
Procedure for ordering:
  Start with leftmost digit as first position
  Before increasing the order in the first position, select the lowest digit in the second position
  Continue the process till the lowest digit in the last position is captured
  Increase the order in the last position until all the digits in the last position are captured
  Move back to the last but one position and repeat the process
  Continue advancing to the first position until all the numbers are ordered
Tree structure for the above process

## Slide 20: MIB Lexicographic Order
Figure 5.12 MIB for Operation Examples in Figures 5.13 and 5.15
A 3.1
B 3.2
T Z
E
1.1
1.2
2.1
2.2
Notes :

## Slide 21: A More Complex MIB Example
Notes:

## Slide 22: Get-Next-Request Operation

## Slide 23: Get-Next-Request Operation

## Slide 24: Sniffer Data

## Slide 25: SNMP MIB
Notes :
SNMPv1 MIB has too many objects that are not used
SNMPv2 obsoleted a large number of them
Nisreen AlGhadban 120015789