## Slide 1: Chapter 11
18-29 محذوف
Network Management Applications
Chapter 11 Network Management Applications
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 2: Objectives
Chapter 11 Network Management Applications
Network Management: Principles and Practice
© Mani Subramanian 2010
Network management and system management
Network management
  Configuration
  Fault
  Performance
  Security
  Accounting
Configuration management
  Configuration management
  Service/Network provisioning
  Inventory management
Fault management
  Fault detection and isolation
  Correlation techniques for root cause analysis
Performance management
  Performance metrics
  Data monitoring
  Problem isolation
  Performance statistics
(continued)
*

## Slide 3: Objectives (cont.)
Chapter 11 Network Management Applications
Network Management: Principles and Practice
© Mani Subramanian 2010
Security management
  Security policies and procedures
  Security threats
  Firewall
  Cryptography: keys, algorithms, authentication, and authorization schemes
  Secure message transfer methods
Accounting management
Report management
Policy-based management
Service level management
  Quality of service, QoS
  Service level agreement, SLA
*

## Slide 4
  Notes
Network and Systems Mgmt
TMN architecture expanded to include systems management
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 5
  Notes
Management Applications
OSI Model
  Configuration
  Performance
  Fault
  Security
  Accounting
Reports
Service Level Management
Policy-based management
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 6
  Notes
Configuration Management
Network Provisioning
Inventory Management
  Equipment
  Facilities
Network Topology
Database Considerations
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 7
  Notes
Circuit Provisioning
Network Provisioning
  Provisioning of network resources
    Design
    Installation and maintenance
  Circuit-switched network
  Packet-switched network, configuration for
    Protocol
    Performance
    QoS
  ATM networks
Examples:
  TIRKS (Trunk Integrated Record Keeping System) for circuit-switched networks
  E1 in TIRKS for equipment management
  F1 in TIRKS for facilities management
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 8
  Notes
Network Topology
Manual
Autodiscovery by NMS using
  Broadcast ping
  ARP table in devices
Mapping of network
  Layout
  Layering
Views
  Physical
  Logical
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 9
  Notes
Traditional LAN Configuration
One-to-one mapping between physical and logical configuration
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 10
  Notes
Virtual LAN Configuration
Physical and logical configurations different
Physical location obtained from System group
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 11
  Notes
Fault Management
Fault is a failure of a network component
Results in loss of connectivity
Fault management involves:
  Fault detection
    Polling
    Traps: linkDown, egpNeighborLoss
  Fault location
    Detect all components failed and trace down the tree topology to the source
    Fault isolation by network and SNMP tools
    Use artificial intelligence / correlation techniques
  Restoration of service
  Identification of root cause of the problem
  Problem resolution
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 12
  Notes
Performance Management
Tools
Performance Metrics
Data Monitoring
Problem Isolation
Performance Statistics
Tools:
  Protocol analyzers
  RMON
  MRTG
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 13
  Notes
Performance Metrics
Macro-level
    Throughput
    Response time
    Availability
    Reliability
Micro-level
    Bandwidth
    Utilization
    Error rate
    Peak load
    Average load
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 14
  Notes
Traffic Flow Measurement
Network Characterization
Four levels defined by IETF (RFC 2063)
Three measurement entities:
  Meters gather data and build tables
  Meter readers collect data from meters
  Managers oversee the operation
Meter MIB (RFC 2064)
NetrMet - an implementation (RFC 2123)
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 15
  Notes
Data Monitoring and
Problem Isolation
Data monitoring
  Normal behavior
  Abnormal behavior (e.g., excessive collisions, high packet loss, etc.)
  Set up traps (e.g., parameters in alarm group in RMON on object identifier of interest)
  Set up alarms for criticality
  Manual and automatic clearing of alarms
Problem isolation
  Manual mode using network and SNMP tools
  Problems in multiple components need tracking down the topology
  Automated mode using correlation technology
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 16
  Notes
Performance Statistics
Traffic statistics
Error statistics
Used in
  QoS tracking
  Performance tuning
  Validation of SLA
  Trend analysis
  Facility planning
  Functional accounting
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 17
  Notes
Event Correlation Techniques
Basic elements
  Detection and filtering of events
  Correlation of observed events using AI
  Localize the source of the problem
  Identify the cause of the problem
Techniques
  Rule-based reasoning
  Model-based reasoning
  Case-based reasoning
  Codebook correlation model
  State transition graph model
  Finite state machine model
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 18
  Notes
Rule-Based Reasoning
Knowledge base contains expert knowledge on problem symptoms and actions to be taken if -> then condition -> action
Working memory contains topological and state information of the network; recognizes system going into faulty state
Inference engine in cooperation with knowledge base decides on the action to be taken
Knowledge Base executes the action
Process is interactive
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 19
  Notes
Rule-Based Reasoning
Rule-based paradigm is an iterative process
RBR is “brittle” if no precedence exists
An exponential growth in knowledge base poses problem in scalability
Problem with instability if packet loss < 10% alarm green if packet loss => 10% < 15% alarm yellow if packet loss => 15% alarm red Solution using fuzzy logic
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 20
  Notes
Configuration for RBR Example
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 21
  Notes
RBR Example
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 22
  Notes
Model-Based Reasoning
Object-oriented model
Model is a representation of the component it models
Model has attributes and relations to other models
Relationship between objects reflected in a similar relationship between models
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 23
  Notes
MBR Event Correlator
Example:
Recognized by Hub 1 model
Hub 1 model queries router model
Hub 1 fails
Router model
declares failure
Hub 1 model
declares NO failure
Router model
declares no
failure
Hub 1 model
declares Failure
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 24
  Notes
Case-Based Reasoning
Unit of knowledge
  RBR rule
  CBR case
CBR based on the case experienced before; extend to the current situation by adaptation
Three adaptation schemes
  Parameterized adaptation
  Abstraction / respecialization adaptation
  Critic-based adaptation
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 25
  Notes
CBR: Matching Trouble Ticket
Example: File transfer throughput problem
Trouble ticket in case library: A = f(F)
Parameter A is a function of Parameter F
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 26
  Notes
CBR: Parameterized Adaptation
A = f(F)
A’ = f(F’)
Functional relationship f(x) remains the same
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 27
  Notes
CBR: Abstraction / Respecialization
Two possible resolutions
  A = f(F) Adjust network load level
  B = g(F) Adjust bandwidth
Resolution based on constraint imposed
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 28
  Notes
CBR: Critic-Based Adaptation
Human expertise introduces a new case
N (network load) is an additional parameter added to the functional relationship
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 29
  Notes
CBR-Based Critter
CRITTER is CBR-based trouble resolution system
Integrated with Cabletron Spectrum NMS
“Propose” is additional (5th) module to CBR architecture; permits manual intervention
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 30
  Notes
Codebook Correlation Model:
Generic Architecture مهم
Yemini, et. al. proposed this model
Monitors capture alarm events
Configuration model contains the configuration of the network
Event model represents events and their causal relationships
Correlator correlates alarm events with event model and determines the problem that caused the events
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications
Figure 11.18 Generic Architecture of an Event Correlation System

## Slide 31
  Notes
Codebook Approachمهم
Correlation algorithms based upon coding approach to even correlation
Problem events viewed as messages generated by a system and encoded in sets of alarms
Correlator decodes the problem messages to identify the problems
Approach:
Two phases:
1. Codebook selection phase: Problems to be monitored identified and the symptoms they generate are associated with the problem. This generates codebook (problem-symptom matrix)
2. Correlator compares alarm events with codebook and identifies the problem.
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 32
  Notes
Causality Graph
Each node is an event
An event may cause other events
Directed edges start at a causing event and terminate at a resulting event
Picture causing events as problems and resulting events as symptoms
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 33
  Notes
Labeled Causality Graph
Ps are problems and Ss are symptoms
P1 causes S1 and S2
Note directed edge from S1 to S2 removed; S2 is caused directly or indirectly (via S1) by P1
S2 could also be caused by either P2 or P3
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 34
  Notes
Codebook
Codebook is problem-symptom matrix
It is derived from causality graph after removing directed edges of propagation of symptoms
Number of symptoms => number of problems
2 rows are adequate to uniquely identify 3 problems
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications
Figure 11.21 Codebook for Figure 11.20

## Slide 35
  Notes
Correlation Matrix
Correlation matrix is reduced codebook
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications
Figure 11.22 Correlation Matrix for Figure 11.20

## Slide 36
  Notes
Correlation Graph
Correlation graph is derived from correlation matrix
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 37
  Notes
Generalized Causality Graph
Causality graph has 11 events - problems and symptoms
Mark all nodes that have only emerging directed edges as problems - Nodes 1, 2, and 11
Other nodes are symptoms
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 38
  Notes
P-S Causality Graph
To reduce causality graph to correlation graph:
  Symptoms 3, 4, and 5 are cyclical: replace with one symptom, say 3
  S7 and S10 are caused by S3 and S5 and hence ignored
  S8 causes S9. Keep S9 and eliminate S8; reason for this would be more obvious if we go through reduction of codebook to correlation matrix
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications
Figure 11.24 Generalized Causality Graph

## Slide 39
  Notes
Correlation Graph and Matrix
Note that problems 1 and 11 produce identical symptoms
Figure 11.26 Correlation Matrix for Figure 11.24
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 40
  Notes
Codebook Enhancements
Codebook described so far assumes Hamming distance of 1 for uniqueness
Noise affects accuracy
Increase Hamming distance to >1
Probability of a problem causing a symptom assumed as 1. It can be made Si = Pr(Pj) to be more realistic
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 41
  Notes
State Transition Model
Used in Seagate’s NerveCenter correlation system
Integrated in NMS, such as OpenView
Used to determine the status of a node
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 42
State Transition Model Example
  Notes
NMS pings hubs every minute
Failure indicated by the absence of a response
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 43
State Transition Graph
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 44
  Notes
Finite State Machine Model
Finite state machine model is a passive system; state transition graph model is an active system
An observer agent is present in each node and reports abnormalities, such as a Web agent
A central system correlates events reported by the agents
Failure is detected by a node entering an illegal state
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 45
  Notes
Security Management
Security threats
Policies and Procedures
Resources to prevent security breaches
Firewalls
Cryptography
Authentication and Authorization
Client/Server authentication system
Message transfer security
Network protection security
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 46
  Notes
Security Threats
SNMPv3 addressed security threats using USM (user-based security model)
USM has two modules:
  Authentication module
    Data integrity
    Data origin
  Privacy module
    Data confidentiality
    Message timeliness
    Message protection
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 47
  Notes
Policies and Procedures
References:
  Formal statement of rules for protecting organization’s technology and assets (RFC 2196)
  Introduction to Firewalls (NIST)
  Orange Book by National Computer Security Center (NCSC) rates computers based on security design features
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 48
  Notes
Secure Communication Network
Firewall secures traffic in and out of Network A
Security breach could occur by intercepting the message going from B to A, even if B has permission to access Network A
Most systems implement authentication with user id and password
Authorization is by establishment of accounts
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 49
  Notes
Firewalls
Protects a network from external attacks
Controls traffic in and out of a secured network
Could be implemented in a router, gateway, or a special host
Benefits
  Reduces risks of access to hosts
  Controlled access
  Eliminates annoyance to the users
  Protects privacy (e.g., finger)
  Hierarchical implementation of policy and and technology (e.g., finger)
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 50
  Notes
Packet Filtering Firewall
Uses protocol specific criteria at DLC, network, and transport layers
Implemented in routers - called screening router or packet-filtering routers
Filtering parameters:
  Source and/or destination IP address
  Source and/or destination TCP/UDP port address, such as ftp port 21
Multistage screening - address and protocol
Works best when rules are simple
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 51
  Notes
Application Level Gateway
Firewalls 1 and 2 route traffic only from and to the secured LAN
Secured LAN is gateway LAN
Behavior of application gateway dependent on the application
FTP traffic stored and forwarded after validation
TELNET hosts validated for the session and then direct communication established
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 52
  Notes
Cryptography
Secure communication requires
  Integrity protection: ensuring that the message is not tampered with
  Authentication validation: ensures the originator identification
Security threats
  Modification of information
  Masquerade
  Message stream modification
  Disclosure
Hardware and software solutions
Most secure communication is software based
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 53
  Notes
Secret Key Cryptography
Caesar cipher: each letter replaced by another letter, which is three letters behind in the alphabet
Maximum of 26 attempts to decode Caesar cipher
Monoalphabetic cipher: Replace a letter with another randomly chosen; Maximum attempts to decode 26!
One secret key is needed between each pair
Two standard algorithms for secret key:
  DES (Data Encryption Standard): 64-bit message blocks and 56-bit key
  IDEA (International Data Encryption Algorithm): 64-bit message blocks and 128-bit key
Message block derived using CBC (Cipher Block Chaining)
Principle based on rearranging the blocks several times based on predetermined algorithm and secret key
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 54
  Notes
Public Key Cryptography
Asymmetric cryptography - public and private key
Public key is distributed by the receiver to the senders to encrypt the message.
Private key is used by receiver to decode ciphertext
Mailbox analogy
Commonly used public key is RSA (Rivest, Shamir, and Adleman); 512-bit key, variable block size
RSA less efficient than DES and IDEA; used to encrypt secret key
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 55
  Notes
Message Digest
Message digest is a cryptographic hash algorithm added to a message
One-way function
Analogy with CRC
If the message is tampered with the message digest at the receiving end fails to validate
MD5 (used in SNMPv3) commonly used MD
MD5 takes a message of arbitrary length (32-byte) blocks and generates 128-bit message digest
SHS (Secure Hash Standard) message digest proposed by NIST handles 264 bits and generates 160-bit output
Example:
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 56
  Notes
Digital Signature
Why do we need digital signature?
Principle reverse of public key
Signature created using private key and validated using public key
Digital signature is a message digest generated from plaintext and private key by a hashing algorithm
Digital signature is concatenated with the plaintext and encrypted using public key
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 57
  Notes
Authentication and Authorization
Authentication verifies user identification
  Client/server environment
    Ticket-granting system
    Authentication server system
    Cryptographic authentication
  Messaging environment
    e-mail
    e-commerce
Authorization grants access to information
  Read, read-write, no-access
  Indefinite period, finite period, one-time use
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 58
  Notes
Ticket-Granting System
Used in client/server authentication system
Kerberos developed by MIT
Steps:
  User logs on to client workstation
  Login request sent to authentication server
  AS checks ACL, grants encrypted ticket to client
  Client obtains from TGS service-granting ticket and session key
  Application Server validates ticket and session key, and then provides service
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 59
  Notes
Authentication Server
Architecture of Novell LAN
Authentication server does not issue ticket
Login and password not sent from client workstation
User sends id to central authentication server
Authentication server acts as proxy agent to the client and authenticates the user with the application server
Process transparent to the user
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 60
  Notes
Message Transfer Security
Messaging one-way communication
Secure message needs to be authenticated and secured
Three secure mail systems
  Privacy Enhanced Mail (PEM)
  Pretty Good Privacy (PGP)
  X-400: OSI specifications that define framework; not implementation specific
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 61
  Notes
Privacy Enhanced Mail
Developed by IETF (RFC 1421 - 1424)
End-to-end cryptography
Provides
  Confidentiality
  Authentication
  Message integrity assurance
  Nonrepudiation of origin
Data encryption key (DEK) could be secret or public key-based originator and receiver agreed upon method
PEM processes based on cryptography and message encoding
  MIC-CLEAR (Message Integrity Code- CLEAR)
  MIC-ONLY
  ENCRYPTED
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 62
  Notes
PEM Processes
DEK a random number generated per message basis: used to encrypt the message text and generate MIC
IK a long-range key agreed upon between the sender receiver used to encrypt DEK: IK is either public or secret
Public key avoids repudiation
(Originating end)
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 63
  Notes
Pretty Good Privacy
PGP secure mail package developed by Zimmerman
Available in public domain
Signature generation
  Uses MD5 to generate hash code
  Encrypts hash code with sender’s private key using RSA algorithm
Encryption of the message done using IDEA or RSA
Compression done with ZIP
email conversion done using Radix-64
PGP similar to encrypted PEM with added compression
(Originating end)
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 64
  Notes
SNMPv3 Security
(Outgoing message)
Authentication key equivalent to DEK in PEM or private key in PGP
Authentication key generated using user password and SNMP engine id
Authentication key may be used to encrypt message
USM prepares the whole message including scoped PDU
HMAC, equivalent of signature in PEM and PGP, generated using authentication key and the whole message
Authentication module provided with authentication key and HMAC to process incoming message
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 65
  Notes
Virus Attacks
Executable programs that make copies and insert them into other programs
Attack hosts and routers
Attack infects boot track, compromises cpu, floods network traffic, etc.
Prevention is by identifying the pattern of the virus and implementing protection in virus checkers
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 66
  Notes
Accounting Management
Least developed
Usage of resources
Hidden cost of IT usage (libraries)
Functional accounting
Business application
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 67
Report Management
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 68
  Notes
Policy-Based Management
Domain space consists of objects (alarms with attributes)
Rule space consists of rules (if-then)
Policy Driver controls action to be taken
Distinction between policy and rule; policy assigns responsibility and accountability
Action Space implements actions
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications

## Slide 69
  Notes
Service Level Management
SLA management of service equivalent to QoS of network
SLA defines
  Identification of services and characteristics
  Negotiation of SLA
  Deployment of agents to monitor and control
  Generation of reports
SLA characteristics
  Service parameters
  Service levels
  Component parameters
  Component-to-service mappings
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 11 Network Management Applications