## Slide 1: Chapter 12
Broadband Network Management: WAN
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 2: Objectives
Broadband WAN segment
  IP (has been dealt with earlier)
  ATM
  MPLS
  Optical and MAN feeder network
ATM
  Virtual path–virtual circuit (VP-VC) operation
  Real-time and non-real-time function for broadband service
  ATM as public and private switched networks
  Emulated LAN configuration
  ATM management: M1, M2, M3, and M4 interfaces
  ATM digital exchange interface management
MPLS
  Possesses rich features of IP and good performance of ATM
  Basic principles of label switching
  Label switched path, LSP
  Traffic engineering
  MPLS OAM
  Service level management
  MPLS MIBs
  MPLS TE MIBs
  MPLS example
Optical and MAN feeder network
  SONET-based MAN
  SONET transport hierarchy
  SDH and (D)WDM network
  SDH management
  WDM management
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 3: Broadband Services
  Notes
Broadband Integrated Services Digital Network (BISDN)
  Voice, video, and data services
  Transport protocol and medium
(Basic) Integrated Services Digital Network (ISDN)
  2B + D
WAN
  ATM Cell-based Technology
  SONET / OC-n (n x 51.84 Mbps)
  SDH / STS
LAN
  ATM LAN Emulation
Access Technology
  Cable modem / HFC
  DSL
  Wireless
Chapter 12 Broadband Network Management: WAN
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 4: Broadband Services Network
  Notes
IP / ATM over MPLS WAN
MAC / PHY layer SDH / SONET
Access Networks
  OC-n used to access institutions
  HFC, DSL and Fixed Wireless to residence
  Limited mobile wireless technology
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Figure 12.1 Broadband Service Networks

## Slide 5: ATM Technology
  Notes
ATM technology based on:
  VP / VC
  Fixed packet size or cell
  Small packet size (53 bytes)
  Statistical multiplexing
  Integrated services
  After initial set up, latency is reduced
  Variable bit rate
  Simultaneous real- and non-real time traffic
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 6: VP - VC
  Notes
Switch | Input VCI / Port | Output VCI / Port
A | VCI-1 / Port-1 VCI-2 / Port-2 | VCI-2 / Port-2 VCI-1 / Port-1
B | VCI-2 / Port-1 VCI-3 / Port-2 | VCI-3 / Port-2 VCI-2 / Port-1
D | VCI-3 / Port-1 VCI-4 / Port-2 | VCI-4 / Port-2 VCI-3 / Port-1
Figure 12.2 Virtual Circuit Configuration
All packets take the same path and arrive in the same sequence in virtual circuit
Packets in a session take the same path in VP/VC
After initial set up, latency is reduced
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Table 12.2 A-Z Virtual Circuit –Routing Tables

## Slide 7: ATM LAN Emulation (LANE)
  Notes
Difference between ATM and Ethernet
  ATM is connection-oriented
  ATM makes one-to-one connection
  ATM 20-byte addressing scheme different from 6-byte Ethernet MAC address
LANE emulates services of a traditional LAN
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 8: ATM WAN Reference Model
  Notes
WAN service provided by public service providers
Private networks use public WAN facilities
Management functions (OAMP)
  Operations
  Administration
  Maintenance
  Provisioning
Public and private User Network Interface (UNI) define user interfaces
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 9: ATM WAN Management
  Notes
Management interface architecture defined by ATM Forum
Public and private NMS responsible to manage respective domains
OSI has defined five management interfaces:
  M1 Interface between private NMS and end user
  M2 Interface between private NMS and network
  M3 Interface between private NMS and public NMS
  M4 Interface between public NMS and network
  M5 Interface between public NMSs
BICI Broadband inter-carrier interface
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 10: Integrated Local Management Interface (ILMI)
  Notes
ATM Forum defines additional interface (ILMI)
  UNI User network interface
  NNI Network-Network interface
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 11: ATM MIB
  Notes
MIBs defined in two sets of documents - IETF (5 nodes) & ATM Forum (1 node)
ATM MIBs address ATM sublayer parameters only
ifMIB contains additional objects not covered in interfaces MIB
atmMIB contains ATM objects
atmForum specifies interfaces, LANE, Mx, and ILMI
atmRMON (experimental) address ATM remote monitoring (covered in Chapter 8)
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Figure 12.6 Internet ATM MIB

## Slide 12: SNMP ATM Management
  Notes
ATM Management specifications available for both SNMP and OSI management implementations
SNMP agent built in ATM device
System, Interfaces, Interface types, transmission carrier groups (T1, T3, SONET), and ATM object groups are monitored
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 13: SNMP and ILMI
  Notes
ILMI MIB used to gather data between ATM devices
Proxy agents convert ILMI objects to SNMP objects
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 14: M1 Interface Management
  Notes
M1 management interface is across an ATM device
Additional MIBs created using ifMIB group to handle sublayers
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 15: ATM Transmission Groups
  Notes
Three transmission modes used for ATM in US
  DS1 1.544 Mbps T1 carrier
  DS3 44.736 Mbps T3 carrier
  SONET n X 155.52 Optical fiber
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 16: ATM Managed Objects Group
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 17: M2 Interface Management
  Notes
M2 interface used to manage private networks
ATM link management data gathered using ILMI MIB
ILMI addresses:
  Administrative information (atmForumAdmin) - registry to locate ATM network services such as LECS and ANS
  UNI
  DXI (Data Exchange Interface)
  LAN Emulation
  NNI
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 18: ATM UNI Group
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 19: M3 Interface
  Notes
Services offered by public NMS to customer on PVCs
Two classes
  Class I: Status and configuration management
  Class II: Virtual configuration control
Class I:
  Functions offered by public NMS to customer - monitoring and management of configuration, fault, and performance
Class II:
  User ability to add, delete, and change VC between customer UNIs
Class I mandatory and Class II optional
Class I examples
  Retrieving performance and configuration for UNI link
  Public NMS reporting of a UNI link failure
Class II examples
  Establishing a new VP
  Increase the number of VCs in a VP
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 20: Customer Network Management (CNM)
  Notes
CNM manages both private and public networks
CNM agent in public network provides M3 service
CNM manages its own ATM networks at sites 1, 3, and 4.
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 21: M3 Class I Management
  Notes
Class I requirements used by customer NMS from carrier NMS
The MIB access is “read-only”
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 22: M3 Class II Management
  Notes
Management information falls into three subgroups
  ATM-level subgroup: configuration modification
  VPC/VCC-level subgroup: configuration modification and status information of VP/VC link and connection
  Traffic subgroup: modification of traffic descriptors and information for VP/VC connections
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 23: ATM Relationship to TMN
  Notes
ITU-T definition of five-layer model to manage telecommunications network
ATM heavily used in WAN, responsibility of public service providers
The bottom three layers apply to ATM management
Reference points are abstract interfaces between layers
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 24: M4 Interface
  Notes
M4 interface defines dual views
  Network element view
  Network view
Two NMSs interface at network view level
Each NMS interfaces with network elements using network element view
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 25: Network Element View
  Notes
Network element view architecture proposed by ATM Forum
Multiple agent layers - SNMP and ILMI agents implied in the representation
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 26: Network View
  Notes
Three-tier architecture
Each subNMS manages its respective domains
SubNMS communicates with MoM at network view level
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 27: Combined NE and Network Views
  Notes
An NMS could function at both levels simultaneously
Local elements can be managed using NE view and remote elements using network view with subNMS
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 28: M4 NE View Requirements: Configuration Management
  Notes
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 29: M4 NE View Requirements: Fault Management
  Notes
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 30: M4 NE View Requirements: Performance Management
  Notes
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 31: M4 Network View Requirements
  Notes
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 32: M4 Network View Requirements: Security Management
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 33: ATM DXI Management
  Notes
Digital Exchange Interface defined between DTE (digital terminating equipment) and DCE (digital circuit equipment)
Example of DTE is hub and DCE is DSU (digital service unit); ATM switch is part of public network
Management of DXI and ATM UNI done using ILMI specifications
NMS manager uses SNMP with proxy agent for ILMI management objects
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 34: Simplified MPLS Network
  Notes
MPLS … Multiprotocol Label Switching combines
  Richness of IP
  Performance of ATM
FEC assigned at the ingress router and encoded in the label
Label is removed at the egress router and original protocol packet is sent out
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Figure 12.21 Simplified MPLS Network

## Slide 35: IP Network
  Notes
FEC (Forward Equivalent Class) decides the port for the next hop
Packets with the same FEC indistinguishable and sent to the same port
FEC determination is complex and done at each node
This leads to low performance (compare with ATM VP-VC achieving high performance)
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Figure 12.22(a) IP Packet Forwarding Based on the FEC Index Table

## Slide 36: MPLS / IP Network
  Notes
FEC assigned at the ingress router and encoded in the label
Label is removed at the egress router and original protocol packet is sent out
Label is sent along with the packet
Label is used as index to look up a table and forward the packet and a new label to the next hop
Packet not analyzed for FEC by downward routers
Header in layer-3 ignored
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Figure 12.22(b) MPLS Packet Forwarding Based on the FEC Index Table

## Slide 37: MPLS / ATM مهم
  Notes
Switch | Input VCI / Port | Output VCI / Port
A | VCI-1 / Port-1 VCI-2 / Port-2 | VCI-2 / Port-2 VCI-1 / Port-1
B | VCI-2 / Port-1 VCI-3 / Port-2 | VCI-3 / Port-2 VCI-2 / Port-1
D | VCI-3 / Port-1 VCI-4 / Port-2 | VCI-4 / Port-2 VCI-3 / Port-1
Figure 12.2 Virtual Circuit Configuration
All packets take the same path and arrive in the same sequence in virtual circuit
Packets in a session take the same path in VP/VC
After initial set up, latency is reduced
Both real- and non-real time traffic handled simultaneously
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Table 12.2 A-Z Virtual Circuit –Routing Tables

## Slide 38: MPLS Traffic Configuration
  Notes
Packets in MPLS with input labels are mapped to next hop with output labels; header in layer 3 ignored
Packet routing configured for MPLS / IP with IGP
with and without TE (traffic engineering) and tunneling
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 39: MPLS / IP without Tunnel
  Notes
Dest | 0utput Interface | Next Hop | Metric
2.2.2.2 | I1 | 2.2.2.2 | 1
3.3.3.3 | I1 | 2.2.2.2 | 2
4.4.4.4 | I1 I2 | 2.2.2.2 6.6.6.6 | 3 3
5.5.5.5 | I1 I2 | 2.2.2.2 6.6.6.6 | 4 4
6.6.6.6 | I2 | 6.6.6.6 | 1
7.7.7.7 | I2 | 6.6.6.6 | 2
8.8.8.8 | I1 I2 | 2.2.2.2 6.6.6.6 | 4 4
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Figure 12.23 Topology without MPLS Tunnels
Table 12.12 R1 Routing Table without Tunnel

## Slide 40: MPLS / IP with Tunnels
  Notes
Dest | 0 Intf | Next Hop | Metric
2.2.2.2 | 1I1 | 2.2.2.2 | 1
3.3.3.3 | 1I1 | 2.2.2.2 | 2
4.4.4.4 | T1 | 4.4.4.4 | 3 /1
5.5.5.5 | T2 | 5.5.5.5 | 4/1
6.6.6.6 | 1I2 | 6.6.6.6 | 1
7.7.7.7 | 1I2 | 6.6.6.6 | 2
8.8.8.8 | T1 | 4.4.4.4 | 4/2
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Figure 12.24 MPLS Topology with Tunnels
Table 12.13 R1 Routing Table with Tunnel

## Slide 41: MPLS-TE
  Notes
Traffic Engineering (TE): Optimization of performance
Overlay over inadequate IGP
  Constrained-base routing at VC level
  VC paths
  Path compression
  Call admission control
  Traffic shaping and policing
  VC survivability
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Figure 12.25 MPLS-TE System Block Diagram (Head-End Router)

## Slide 42: Label Switching Router (LSR)
  Notes
MPLS router called Label Switching Rouer (LSR)
End-to-end MPLS path called Label Switching Path (LSP)
IGP extended to include MPLS-TE
Route set up by RSVP-TE
Control and data planes separated in MPLS
VoIP handled using SIP (Session Initiation Protocol)
*
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 12 Broadband Network Management: WAN

## Slide 43: MPLS Label
  Notes
MPLS Label is
  Short and fixed length – 32 bits
  FEC locally significant identifier
Label assigned by the downstream router
Label is “shimmed” between layers 2 and 3 headers
Exp…experimental
S…….stack indicator
TTL….time-to-live
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 44: MPLS Labeled Packets
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Figure 12.27 Encapsulation of an MPLS-Labeled Packet

## Slide 45: Label Generation
  Notes
Label generated by downstream LSR Rd
Upstream LSR Ru and Rd together generate “label” between label Lx and FEC F
Rd has incoming labels L1 and L2, and outgoing label L3 with FEC F
Label L associated with FEC F is local to Ru and Rd
Ru and Rd called “label binding pair”
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 46: LSP, LSR, Label مهم
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 47: MPLS OAM Management
  Notes
Data and control planes are separate in MPLS
OAM packets travel the data path
Basic Tools
  LSP connectivity verification
  LSP ping
  LSP traceroute
Fault management
Configuration management
Performance management
LSP Fault scenarios:
  (a) Simple loss of connection
  (b) Misconnection
  (c) Swapped connection
  (d) Mismerging
  (e) Loop/unintended replication
Detection of LSP fault using
  connectivity verification (CV) – ITU-T
  Bidirectional forwarding detection (BFD) - IETF
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 48: Fault Management of LSP
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Figure 12.30 MPLS Fault Scenarios

## Slide 49: LSP Ping
  Notes
Table 12.15 MPLS Echo Request Packet
Modified Internet ping
MPLS echo request from Ingress to egress LSR; response from egress LSR on connectivity and validation
Verify packets of specific FEC end their LSP on an LSR that is an egress for that FEC.
Packet travels data path to egress LSR and transferred to control plan
Control plane validates FEC belongs to the egress LSR and sends response
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Byte 1 | Byte 2 | Byte 3 | Byte 4
Version Number |  | Global Flags | 
Message Type | Reply Mode | Return Code | Return Subcode
Sender’s Handle |  |  | 
Sequence Number |  |  | 
TimeStamp Sent (seconds) |  |  | 
TimeStamp Sent (microseconds) |  |  | 
TimeStamp Received (seconds) |  |  | 
TimeStamp Received (microseconds) |  |  | 
TLV |  |  | 

## Slide 50: LSP Traceroute
  Notes
Similar to IP traceroute
Hop-by-hop fault localization as well as path tracing
Packet sent to control plane of each transit LSR
Transit LSR validates LSP
Validates control plane against data plane of the LSR
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 51: Connectivity Verification
  Notes
Top label user packet label
2nd label OAM label with reserved value of 14
Stack bit value 1 indicates bottom label
Ingress LSR sends CV packet with TTSI (trail termination source identifier) – LSP and LSR IDs
CV packets sent asynchronously at regular intervals
On consecutive loss of set number of packets (3) egress LSR declares loss of connectivity (dlOCV)
Other scenarios analyzed by egress LSR and notifications sent
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 52: BFD
  Notes
Bidirectional forwarding failure detection
An IETF specification (CV is ITU-T spec); more versatile
Uses LSP-ping MPLS echo - response to detect data plane failure in LSP
Helpful to detect failures in the data plane when the control plane is functional and data plane is not
Establishes session between ingress and egress LSRs
Verification packet can be used at any protocol layer
Fast and low overhead detection between adjacent NEs
BFD fault detection interval should be longer than switching time in the fast-reroute LSP
Separate session for multiple FECs in an LSP
LSP traceroute used for data path check in alternate paths
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 53: LSP Self-Test
  Notes
Used for fault localization of an LSP
Uses 3 LSRs, ST (self test), LSR-U upstream, and LSR-D downstream
LSR-ST sends special LSP-ping to LSR-U with TTL=3
LSR-U forwards it via LSR-ST to LSR-D with TTL=2
LSR-D sends reply to LSR-ST completing the test
Fault localized for link and node failures and notification sent out
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Figure 12.32 LSP Self-Test

## Slide 54: MPLS Service Level Management
  Notes
R1
R2
R3
R4
R5
R6
Customer
Net A
Customer
Net B
LSP 2
LSP 1
LSP 1 PROTECTION
SLA between Service Provider and customer
Multiple protection paths
LSP1 PROTECTION global protection
Nested path LSP 2 local protection path
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Figure 12.33 LSP Nesting and Fault Localization

## Slide 55: MPLS MIB OID Tree
  Notes
MPLS network has a range of MIB modules
Complex and interdependent modules
Two nodes under transmission (mib-2 10)
  mplsstd MIB…MPLS OID group
  teLinkstdMIB…MPLS Traffic engineered links
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 56: MPLS MIBs
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
  Notes
MPLS-LSR-STD-MIB heart of the MPLS manage- ment architecture
MPLS-LSR-STD-MIB describes managed objects for modeling MPLS LSR and comprises:
  Label-forwarding info base (LFIB) -> View of LSP being switched by the LSR
  Cross-connects and their properties referred in other MPLS MIBs
Entity | OID | Description (brief)
mplsStdMIB | transmission (166) | MPLS OID Group
mplsTCStdMIB | mplsStdMIB (1) | Defines textual conventions
mplsLsrStdMIB | mplsStdMIB (2) | LSR Managed Objects (MO)
mplsTeStdMIB | mplsStdMIB (3) | Traffic Engineered Tunnel MO
mplsLdpStdMIB | mplsStdMIB (4) | Label Distribution Protocol (LDP) MO
mplsLdpAtmStdMIB | mplsStdMIB (5) | MO used with MPLS-LDP-STD-MIB for MPLS/ATM as layer 2
mplsLdpFrameRelayStdMIB | mplsStdMIB (6) | MO used with MPLS-LDP-STD-MIB for MPLS/Frame Relay as layer 2
mplsLdpGenericStdMIB | mplsStdMIB (7) | LDP Per Platform Label Space reserved for other platforms
mplsFTNStdMIB | mplsStdMIB (8) | FTN MO (FEC-to-NHLFE (Next Hop Label Forwarding Entry)
Table 12.16 MPLS Object Identifier (OID) MIB Group

## Slide 57: MPLS MIB Dependencies
  Notes
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Arrow indicates “depends on” relationship
All MIBs depend on MPLS-TC-STD-MIB that defines textual convention
External dependencies on IF-MIB

## Slide 58: MPLS MIB Group Composition
  Notes
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
MPLS Group comprise:
  Tables
  Scalars provide the next available index to generate a row
  Indices are arbitrary
Table 12.17 MPLS LSR Tables
Table | OID | Functions
Interface configuration | mplsInterfaceTable | Enables MPLS interface
In-segment | mplsInSegmentTable | Enables and monitors LSP segments into LSR
Out-segment | mplsoutSegmentTable | Enables and monitors LSP segments out of LSR
In-segment Mapping | mplsInSegmentMapTable | Lookup table for discovery of an in-segment in In-segment table
Cross-connect | mplsXCTable | Associate in and out segment for an LSP
Label stack | mplsLabelStackTable | Specifies multi-label stacks on LSP
In-segment performance | mplsInSegmentPerfTable | Measures performance of LSP
Out-segment performance | mplsOutSegmentPerfTable | Measures performance of LSP
Interface performance | mplsInterfacePerftable | Measures performance on a per-interface basis.

## Slide 59: MPLS Stack Table
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN

## Slide 60: Traffic Engineering Link MIB
  Notes
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Entity | OID | Description (Brief)
teLinkStdMIB | transmission (200) | MPLS Traffic Engineered Links MO
teLinkNotifications | teLinkStdMIB(0) | Event notifications MO
teLinkObjects | teLinkStdMIB(1) | Traffic Engineered Link MO
teLinkConformance | teLinkStdMIB(2) | MPLS compliance MIB
TE-LINK-STD-MIB used for modeling and managing TE links
Aggregates similar data channels or TE links between pairs of LSRs
A TE link is a sub-interface capable of carrying TE MPLS traffic
Bundled link bonds traffic of a group of TE links
Table 12.18 Traffic Engineering Link MIB Group

## Slide 61: MPLS Example with LSP Path
  Notes
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Table 12.19 LER-1 MPLS Out-Segment Table for LSP
mplsoutSegmentIndex | 1
mplsoutSegmentInterface | 2
mplsoutSegmentPushTopLabel | 
mplsoutSegmentTopLabel | 13
mplsoutSegmenttopLabelPointer | 0.0 (no external table pointer)
mplsoutSegmentNextHopAddrType | 1 (IPv4)
mplsoutSegmentNextHopaddr | 2.2.2.1
mplsoutSegmentXCIndex | mplsXCTable.1
mplsoutSegmentOwner | LER-2
mplsoutSegmentTrafficParam | 0.0 (for best effort)

## Slide 62: MPLS Example (cont.)
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Table 12.20 LER-1 MPLS Cross-Connect Table
mplsXCIndex | 1
mplsXCInSegmentIndex | 0
mplsXCOutSegmentIndex | 1
mplsXCLspId | 4 (LSP Id forward path from LER-1 to LER-R3)
mplsXCLabelStackIndex | 0 (only one outgoing label)
mplsXCOwner | LER-1
Table 12.21 MPLS LSR-C Core In-Segment Table
mplsoutSegmentIndex | 1
mplsoutSegmentInterface | 2
mplsoutSegmentPushTopLabel | True (1) for tunnel
mplsoutSegmentTopLabel | 14
mplsoutSegmenttopLabelPointer | 0.0 (no external table pointer)
mplsoutSegmentNextHopAddrType | 1 (IPv4)
mplsoutSegmentNextHopaddr | 4.4.4.4 (Tunnel/LSP destination)
mplsoutSegmentXCIndex | mplsXCTable.1
mplsoutSegmentOwner | LSR-C
mplsoutSegmentTrafficParam | 0.0 (for best effort)

## Slide 63: MPLS Example (cont.)
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Table 12.22 MPLS LSR-C Core Out-Segment Table
mplsoutSegmentIndex | 1
mplsoutSegmentInterface | 2
mplsoutSegmentPushTopLabel | 
mplsoutSegmentTopLabel | 13
mplsoutSegmenttopLabelPointer | 0.0 (no external table pointer)
mplsoutSegmentNextHopAddrType | 1 (IPv4)
mplsoutSegmentNextHopaddr | 3.3.3.1
mplsoutSegmentXCIndex | mplsXCTable.1
mplsoutSegmentOwner | LER-C
mplsoutSegmentTrafficParam | 0.0 (for best effort)
Table 12.23 MPLS LSR-C Core Cross-Connect Table
mplsXCIndex | 1
mplsXCInSegmentIndex | 0
mplsXCOutSegmentIndex | 1
mplsXCLspId | 13 (LSP Id forward path from R1 to R4)
mplsXCLabelStackIndex | 0 (only one outgoing label)
mplsXCOwner | LSR-C

## Slide 64: MPLS Example (cont.)
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Table 12.24 MPLS LER-2 In-Segment Table
mplsInSegmentIndex | 1
mplsInSegmentInterface | 1
mplsInSegmentLabel | 0 (if no external LabelPointer)
mplsInSegmentLabelPointer | 0.0
mplsInSegmentNPop | 1
mplsInSegmentAddrFamily | 1 (IPv4)
mplsInSegmentXCIndex | 1 (given)
mplsInSegmentTrafficParam | 0.0
Table 12.25 MPLS LER-2 Cross-Connect Table
mplsXCIndex | 1
mplsXCInSegmentIndex | 1
mplsXCOutSegmentIndex | 0
mplsXCLspId | 4 (LSP Id forward path from R1 to R4)
mplsXCLabelStackIndex | 0 (only one outgoing label)
mplsXCOwner | R1

## Slide 65: Optical Metropolitan Area Network (MAN)
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
  Notes
MAN…segment that connects WAN to Access Network
Wired (incl fiber) and wireless (WiMax) MAN
Wired MAN evolved from digital loop carrier (DLC)
Link SONET (synchronous optical network) ring using SDH (synchronous digital hierarchy)
STM-1 (synchronous transport module level 1) @155.52 Mbps. STM-4 @ 622.08 Mbps (OC-3), etc.
RT is add-drop multiplexer (ADM)
Protocol is RPR (resilient packet ring)
RTs connected to access networks

## Slide 66: Dual Ring Configuration
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Failure recovery mode in dual ring configuration
SONET/SDH OC-1 or STS (51.84 Mbps) signal multiplexed to higher level (e.g.,OC-3) and transmitted over optical carrier
WDM (wavelength division multiplexer) strictly a physical layer (optical) system
WDM directly interfaces with the switch
DWDM (Dense WDM) higher density over fiber
  Notes

## Slide 67: Broadband MAN
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
  Notes

## Slide 68: SDH Management
  Notes
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
ITU-T G Series documentation
  Transmission Systems and Media
  Digital Systems and Networks
  Digital Terminal Equipments
G.774 SDH
  Management Information Model
  OAM
  Data Communication Channels (DCCs)
G.784 Element Management Functions (EMFs)
G.831 Management capabilities of transport networks

## Slide 69: SDH Data Communication Channels
  Notes
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
G.774 specifies 3 modes of management for DCCs
  IP-only stack use PPP as data link
  OSI-only use LAP-D as data link
  Dual (IP + OSI) stack PPP or LAP-D with tunneling to communicate between stacks

## Slide 70: SDH Element Management Functions
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
G.784 specs equipment management functions (EMF)
  Fault management
  Performance management
  Configuration management
Two DCC channels
  DCCM forwards over the multiplex sections: behaves as backbone network
  DCCR (and LAN) forwards data to regenerators: interconnects backbone to equipment
  DCCM and DCCR carry independent management applications
  Notes

## Slide 71: SDH Fault Management
  Notes
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
Alarm messages called ”defects”
Error messages called “anomalies”
Loss of signal (LOS) alarm triggers subsequent messages, alarm indication signals (AIS)
Transmitter notified by return of an RDI (remote defect indicator) alarm

## Slide 72: SDH Performance Management
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
  Notes
Performance parameters quantified in G.826
Four commonly used parameters:
  Errored seconds (ES)
    # 1-second intervals containing at least 1 ES
  Severely errored seconds (SES)
    # 1-second intervals with > 30% block errors (or) one severely disturbed period
  Background block error (BBE)
    Errored block that is not SES
  Unavailable seconds (UAS)
    Circuit unavailable from the first of at least 10 consecutive SESs

## Slide 73: SONET Hierarchy and IF Stack Layers
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Chapter 12 Broadband Network Management: WAN
VC-n …Virtual container (Europe)
VT-n … Virtual tributary (America & Japan)