## Slide 1: S 11-32 76-? Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 13
*

## Slide 2: Objectives
*
(Wired) Broadband access networks
  Cable or HFC (hybrid fiber cable) network
  ADSL (asymmetrical digital subscriber line) network
  PON (passive optical network)
Cable access network
  Popular in North American continents
  “Triple play” service can be provided
  DOCSIS (data over cable system interface specifications) standards
ADSL
  Predominant throughout the rest of the world
  Uses conventional telephone local loop medium
  Broadband voice and data services
  Adopts IETF and DSL forum standards
  VDSL2 for performance improvement of broadband service
PON
  PON deployment configurations
  Ethernet-based PON, EPON
  EPON protocol architecture
  EPON management
  EPON MIBs
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010

## Slide 3: Broadband Access Networks
  Notes
Access network between WAN and home network
Four access network technologies
OC-n an extension of WAN for enterprise
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 4: Broadband Access Technologies
  Notes
Cable popular in North America
ADSL more extensively deployed elsewhere in the world
Wireless:
  Fixed: MMDS, LMDS, and WiMax
  Mobile: CDMA, GPRS
PON on fiber medium
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 5: Cable Access Network
  Notes
Head end:
  Signals from multiple sources multiplexed
  Frequency conversion for local signal
Traffic Flow:
  Downstream: Head end to NIU
  Upstream: NIU to head end
Network interface device (NID) / unit (NIU): Demarcation point between customer network and service provider networks
Cable modem: RF Ethernet, voice-over-IP, and video
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 13
*

## Slide 6: Comparative Speeds
  Notes
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Table13.1 Comparative Data Transmission Speeds
*

## Slide 7: Cable Access Network Technology
  Notes
Broadband 2-way cable access network
Asymmetric bandwidth allocation for 2-way communication
Transmission Mode
  Downstream: TDM broadcast mode
  Upstream: TDMA / S-CDMA
RF spread-spectrum that carries multiple signals over HFC
RF spectrum allocation to carry multimedia services - voice, video, and data
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 8: Cable Access Network
  Notes
Single physical medium, 2 logical data streams
Downstream 6 MHz (North American) / 8 MHz (Europe, Asia) channels
Upstream Variable speed channels 160 kbps to 5.2 Mbps
Downstream TDM broadcast mode
Upstream TDMA in DOCSIS 1.0 and 1.1
Upstream S-CDMA in DOCSIS 2.0
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Figure 13.4 Two-way Transmission in a Coaxial Cable
*

## Slide 9: Digital-to-Analog Encoding
  Notes
bit rate
symbol (baud) rate
number of levels n = 2k; k..number of bits per symbol
bit rate = symbol rate x k
Carrier
Carrier
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 10: Modulation Schemes
  Notes
Basic modulation techniques
  ASK (Amplitude Shift Keying)
  FSK (Frequency Shift Keying)
  PSK (Phase Shift Keying)
Cable technology uses
  QPSK (Quadrature Phase Shift Keying)
  QAM (Quadrature Amplitude Modulation)
Quadrature phase shift keying
  Four levels ( 00, 01, 10, 11)
  Relatively insensitive to noise
  Used for low-band upstream
  8 MHz channel: 8x2=16 Mbps
Quadrature amplitude modulation (not 4-levels)
  Combination of AM and PM
  16-QAM = 8 PM x 2 AM or 4 PM x 4 AM
  Used for higher-band downstream
  8 MHz channel 8x4=32 Mbps
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 11: Cable Modem
  Notes
HFC uses tree topology
Downstream in broadcast mode
Upstream transmission by cable modem coordinated by head end
Data-over-cable service specifications (DOCSIS) for cable modem ensures interoperability
One-way cable modem uses telco-return
Table 13.2 Cable Modem Speeds
Version | DOCSIS |  | EuroDOCSIS | 
 | Downstream Mbit/s | Upstream Mbit/s | Downstream Mbit/s | Upstream Mbit/s
1.x | 42.88 (38) | 10.24 (9) Mbit/s | 55.62 (50) | 10.24 (9)
2.0 | 42.88 (38) | 30.72 (27) | 55.62 (50) | 30.72 (27)
3.0 4 channel | +171.52 (+152) | +122.88 (+108) | +222.48 (+200) | +122.88 (+108)
3.0 8 channel | +343.04 (+304) | +122.88 (+108) | +444.96 (+400) | +122.88 (+108)
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 12: Functions of Cable Modem Termination System
  Notes
Equipment at the head end
All cable modems terminated on the head end
Gateway to the external network
Multiplexes and demultiplexes signals
Frequency converts upstream to downstream signals
Can be configured either as a bridge or router
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 13: HFC Plant
  Notes
Multiple fiber pairs run from head end to fiber node; each pair carries 2 one-way signals
Head end converts all (telephony, digital video, data, and analog video) signals to optical carrier to transmit on the fiber
Houses are connected from fiber node via coaxial cables
Coaxial cable is in tree topology and carries 2-way signal
Amplifiers on the coaxial cable have 2-way amplifiers that amplify the signals in both directions
Drop from coaxial cable to NID (also called NIU) - called “Tap-to-TV” in CATV
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 14: RF Spectrum
  Notes
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 15: Data-over-Cable Standards
  Notes
Standards driven by CableLabs
Two sets of standards to achieve interoperability
  DOCSIS (Data-Over-Cable Interface Specifications)
    DOCSIS 1.0
    DOCSIS 1.1
    DOCISS 2.0
    DOCISS 3.0
  IETF RFCs on MIBs
CableLabs Projects
Open Cable: Specifies customer device, Hardware and software
Packet Cable: Interoperable specifications for multimode real-time devices
Cable Home: Interface specifications for extending DOCSIS services to home
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 16: DOCS Reference Architecture
Source: CableLabs
  Notes
The architecture shows two-way (HFC link) and one-way (HFC link & telco return).
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Figure 13.9 Data-Over-Cable System Reference Architecture
*

## Slide 17: CMTS Components
  Notes
Switch / router routes the traffic between cable modems and to the external network. It interfaces to CMTS via the terminator (term).
Modulator (mod) and demodulator (demod) transform digital data from and to analog format.
Combiner and splitter and filter perform the complementary functions of mux’ing and demux’ing.
Transmitter converts the RF signals to optical carrier; receiver down-converts the optical signal.
Servers handle the applications and databases.
Security is managed by the security and access controller.
OSS and element manager perform network and service management.
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 18: DOCS Interfaces
  Notes
Three groups of interfaces:
  Data interfaces
    Cable modem to CPE (1)
    CMTS-NSI (2)
  Operations support systems and telco-return
    OSS (3)
    Telco-return (4)
  RF and security
    DOCS security system (5)
    RF interface (6)
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 19: HFC Management: Challenges
  Notes
More complex than either computer network or telecommunication network
Involves both physical and data layers
Multiple physical facilities
Legacy cable system
Multimedia service
RF spectrum management
Service and business management important for MSOs and customer
Shared media impacts security and bandwidth
Security and privacy of home network
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 20: HFC Protocol Architecture
  Notes
Head end has both NM applications and manager
Cable modems have SNMP agents
NMS can be regionalized; then, head ends could behave as RMONs
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Figure 13.10 Protocol-Layer Architecture in a Cable Access Network System
*

## Slide 21: HFC / CM Management
  Notes
Cable modem management
CMTS management
HFC link management
RF spectrum management
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 22: CM Management MIBs
  Notes
Three categories of MIBs
  Standard MIBs:
    system, interfaces, ifMIB
  CM and CMTS interfaces
    docIfMIB .. RF Interfaces in CM and CMTS, base line privacy and QoS
    docsTrCmMIB .. telephony-return interface
  CM and CMTS objects
    docsDev MIB
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 23: DOCS Interface MIB
  Notes
docsIfMIB supplements standard SNMP interfaces MIB
Covers:
  CM and CMTS objects docsIfMIBObjects
  Baseline privacy MIB docsBpiMIB: Security &
  Privacy
  QoS MIB docsQosMIB: CM and CMTS QoS
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Figure 13.12 DOCS Interface MIB
*

## Slide 24: RF MAC Interface
  Notes
Multiple RF channels upstream and downstream
Layered structure
Specified using RFC 2873 ifMIB
ifType
  docsCable MAC layer 127
  docsCable downstream 128
  docs upstream 129
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Figure 13.13 RF MAC Interface
*

## Slide 25: DOCS Cable Device MIB
  Notes
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Figure 13.14 DOCS Cable Device MIB
*

## Slide 26: DOCS Cable Device MIB
  Notes
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Table 13.6 DOCS Cable Device MIB
*

## Slide 27: Link and Spectrum Management
  Notes
HFC Link Management
  Signal strength critical
  Requires continuous monitoring of amplifiers using transponders (CheetahNet)
  Legacy system requires proxy server
RF Spectrum Management
  Allocation of spectrum for services - upstream and downstream
  Frequency agility management
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 28: DOCSIS 1.0 / 1.1
  Notes
Key differences between DOCSIS 1.0 and 1.1
  Quality of Service – 8 levels
  Dynamic Services
  Fragmentation of upstream packet per CM basis
  Concatenation of packets
  Payload Header Suppression of repeated header
  IP Multicast using IGMP
  CM Authentication
  SNMPv3 security
  View-based access control and management (VACM)
  CM Account Management
  Fault Management
  Secure Software
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 29: DOCSIS 2.0 and 3.0
  Notes
DOCSIS 2.0
  Enhancements on improving the performance of upstream traffic
  Efficient modulation techniques using two protocols:
    Synchronous CDMA (code division multiple access)
    Asynchronous TDMA (time division multiple access)
DOCSIS 3.0
  Introduction of IPv6 management
  Enhanced OSS interface
  Accounting management – Usage-based billing:
    SAMIS (Subscriber Account Management Interface Specification)
  IP Multicast
  Channel bonding
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 30: DOCSIS Documentation (Management Related)
SP-CMCI-I10-050408 | Cable Modem to Customer Premises equipment Interface (CMCI) Specification
SP-CMTRI-I01-970804 | Cable Modem Telephony return Interface Specification
CM-SP-L2VPN-I08-080522 SP-CMTS-NSI-I01-960702 | Cable Modem Termination System - network side Interface specification
SP-RFIv1-I01-990311 CM-SP-DRFI-I06-080215 | RF Interface Specification
CM-SP-BPI+-I12-050812 | Baseline Privacy Interface Specification
CM-SP-OSSIv1.1-C01-050907 CM-SP-OSSIv2.0-I09-050812 CM-SP-M-OSSI-I07-071206 CM-SP-OSSIv3.0-I07-080522 | OSS Interface Specifications
RFC 4639 | Cable Device MIB
RFC 4547 | Event Notification MIB
RFC 4546 | RF Interface MIB
RFC 3083 RFC 4131 | Baseline Privacy MIB
draft-ietf-ipcdn-qos-mib-07.txt RFC 4323 | Quality of Service MIB
draft-ietf-ipcdn-tri-mib-00.txt, July 30, 1998 | Telephony-return interface MIB for Cable Modems and CMTS
RFC 4036 | CMTS for Subscriber Management
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 31: Packet Cable VoIP
  Notes
Packet Cable defines a platform to deliver IP services over DOCSIS
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 32: Packet Cable Multimedia
  Notes
Platform for multimedia over DOCSIS access network
Application manager requests QoS on behalf of clients
Policy managers authorize and commit QoS requests
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 33: Digital Subscriber Line Access Networks
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 34: DSL Access Technology
  Notes
Why is DSL attractive?
Shannon limit of data rate is 30,000 bps (3-KHz, 30 dB S/N channel)
Digital transmission over loop (DSL) improves data rate
  8-15 Mbps downstream
  0.8-1.5 Mbps upstream
  Limit on distance: max to 18,000 feet
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 35: DSL Limitations
  Notes
Loop conditions with no direct copper to the house
Loaded coils in loop (used to increase analog distance) cannot carry digital signal
Modern subdivisions have fiber to the neighborhood or curb with digital mux
Operating company inventory dated (administrative issue)
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 36: xDSL Technologies
  Notes
Name | Meaning | Max Data Rate* | Mode | Cable | Applications
ADSL / ADSL2 / ADSL2+ | Asymmetric Digital Subscriber Line | 7/12/24 Mbps 0.8/1/1 Mbps | Down Up | 1-pair | Most common type
SHDSL | Symmetric High data rate DSL | 5.6 Mbps | Duplex Duplex | 2-pair | Business Connections
VDSL 1 Km | Very high data rate Digital Subscriber Line | 55 Mbps 15 Mbps | Down Up | 2-pair | Triple Play (No QoS)
VDSL2- Long Reach 3 Km | Very high data rate Digital Subscriber Line | 55 Mbps 30 Mbps | Down Up | 2-pair | Triple Play
VDSL Short Reach 500 m | Very high data rate Digital Subscriber Line | 100 Mbps 100 Mbps | Down Up | 2-pair | Triple Play
* Max Data Rate as per Broadband Forum
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Table 13.8 DSL Technologies
*

## Slide 37: ADSL Network
  Notes
ADSL .. Asymmetric Digital Subscriber Line
ATU-C ADSL transmission unit - central office
ATU-R ADSL transmission unit - remote/residence
Splitter separates voice and data
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 38: ADSL Spectrum Allocation with Guard Band
  Notes
POTS .. Plain old telephone service
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Figure 13.16 ADSL Spectrum Allocationd (FDM)
*

## Slide 39: ADSL Spectrum Allocation with Echo Cancellation
  Notes
Echo cancellation separates upstream and downstream signals
Increases (low-frequency) upstream bandwidth
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Figure 13.16 ADSL Spectrum Allocation (Echo Cancellation)
*

## Slide 40: Modulation Schemes
  Notes
Carrierless amplitude phase (CAP) modulation
Discrete MultiTone modulation (DMT): 4kHz tones
Both CAP and DMT are QAM-based
DMT outperforms CAP
  Higher downstream throughput > 4 times
  Higher upstream throughput > 10
  Rate adaptive
  Ongoing active monitoring
  Maximum loop variation coverage
  Standard and hence interoperability
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 41: DSL / Broadband Forum
  Notes
ADSL (now Broadband) Forum is an industry consortium formed to
  Achieve interoperability
  Accelerate DSL implementation
  Address end-to-end system operation
  Security
  Management
3 sets of complementary standards adopted
  ITU-T standards
    G.992.x
    G.997.x
    T1-413 (ANSI)
  Forum Standards
    Technical reports TR-xxx
  IETF standards
    RFC xxxx
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 42: Selected Documentation from DSL / Broadband Forum
TR-001 | ADSL Forum System Reference Model | May 1996
TR-005 | ADSL Network Element Mgmt | March 1998
TR-015 | CAP Line Code Specific MIB | February 1999
TR-024 | DMT Line Code Specific MIB | June 1999
TR-027 | SNMP-based ADSL LINE MIB | September 1999
TR-028 | CMIP Specification for ADSL Network Element Mgmt | May 1999
TR-066 | ADSL Network Element Mgmt (Update to TR-005) | March 2004
TR-090 | Protocol Independent Object Model for Managing Next Generation ADSL Technologies | December 2004
TR-113 | MCM Specific Managed Objects in VDSL Network Element | December 2005
TR-128 | Addendum to TR-090 | September 2006
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Table 13.9 ADSL Management Documents
*
  Notes

## Slide 43: VDSL Network
  Notes
Used in FTTN configuration
Asymmetric band allocation (similar to ADSL)
Fiber carries multiple channels to ONU
Channels demultiplexed at ONU and carried to customer premises on multiple twisted pairs
Shorter distance of multiple twisted pairs
Higher data rate - 55.2 Mbps downstream and 2.3 Mbps upstream
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Figure 13.17 VDSL Access Network
*

## Slide 44: ADSL Network
  Notes
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 45: Transport Modes
  Notes
Synchronous transport mode (STM)
  Bit synchronous transmission (T1/E1)
End-to-end packet mode
  Used for SOHO (IP packets)
ATM / STM
  ATM WAN (Public network) and STM access network
ATM / Packet
  ATM WAN and packet access network (IP)
End-to-end ATM
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 46: ADSL System Reference Model
(ADSL Forum)
  Notes
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 47: Interfaces
  Notes
An interface can have multiple physical connections
V interface
  VC interface between access node and external network and interfaces
U interfaces - off the splitters; Will be eliminated with ADSL-Lite
POTS interfaces – low-pass filter interfaces for POTS
T and B are customer premises network interfaces
  T between PDN and service modules
  B auxiliary data input (e.g., satellite feed)
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 48: ADSL Channeling Schemes
  Notes
Transport bearer channels
  Seven AS downstream channels - multiples (1-, 2-, 3- or 4-) T1 rate of 1.536 Mbps
  Three LS duplex channels - 160, 384, and 576 Kbps
Buffering scheme
  Fast channel: uses fast buffers for real-time data
  Interleaved channel: used for non-real-time data
  Both fast and interleaved channels carried on the same physical channel
ATU-C
ATU-R
Downstream bearer channels
Duplex bearer channels
ATU-C
ATU-R
Fast channel
Interleaved channel
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Figure 13.20 ADSL Channeling

## Slide 49: Management Reference Model
  Notes
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 50: Management Elements
  Notes
Management of elements done across V-interface:
  Management communications protocol across V-interface
  Management communications protocol across U-interfaces
  Parameters and operations across ATU-C
  Parameters and operations across ATU-R
  ATU-R side of the T interface
Note addition of physical layer and switching in the management architecture representation
Management of physical layer involves:
  Physical channel
  Fast channel
  Interleaved channel
Management of type of line encoding
  DMT
  CAP
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 51: Signal Power and Data Rate Management
  Notes
Five levels of noise margin
Signal power controlled by noise margin
Data rate: Increase or decrease based on threshold margins
Data rate adaptation modes: Manual (1), automatic at start-up (2), and dynamic (3)
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 52: Configuration Mgmt Parameters
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Table 13.10 ADSL Configuration Management Parameters

## Slide 53: Fault Management
  Notes
Failure indication of physical channel by NMS
Failure indication of logical channels
Failure indication of ATU-C/R
Self-test of ATU-C/R as per T1.413
Noise margin threshold alarms
Rate change due to noise margin
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Table 13.11 ADSL Fault Management Parameters

## Slide 54: Performance Management
  Notes
Line attenuation
Noise margin
Output power
Data rate
Data integrity check
Interleave channel delay
Error statistics
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Table 13.12 ADSL Performance Management Parameters

## Slide 55: ADSL SNMP MIB
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 56: Proposed IF Types
  Notes
Sublayers handled by ifMIB ifStackTable {ifMib.ifMIBObjects 2} (RFC 1573)
Propose ifTypes adslPhysIf ::= {transmission 94} adslInterIf ::= {transmission 124} adslFastIf ::= {transmission 125}
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 57: ADSL Interfaces Table
  ADSL Operational Configuration
Line type | Physical | Fast Channel | Interleaved Channel
Number of Channels (1) | Yes |  | Yes
Fast only (2) | Yes | Yes | 
Interleave only (3) | Yes |  | Yes
Fast or Interleaved (4) | Yes | Yes | Yes
Fast and Interleaved (5) | Yes | Yes | Yes
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Table 13.13 Use of Interfaces Table for ADSL
Table 13.14 ADSL Operational Profile for ifType File

## Slide 58: ADSL Profiles Management
  Notes
Configuration profile
Performance profile
Alarm profile
Traps
  Generic
  Loss of frame
  Loss of signal
  Loss of power
  Error-second threshold
  Data rate change
  Loss of link
  ATU-C initialization failure
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 59: Configuration Profile: Mode I - Dynamic
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 60: Configuration Profile: Mode II - Static
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 61: ADSL EMS-NMS Management
  Notes
TMN- and ATM-based model
M4 is ATM Forum defined interface between public NMS and public network
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 62: ADSL2 and ADSL2+
Rate and reach Improvements
ADSL Speed Downstream/Upstream 1/.256 Mbps
ADSL2 Standard G.992.3 July 2002
ADSL2 Lite Standard G.992.4 July 2002
  Speed Downstream/Upstream 12/1 Mbps
ADSL2+ Standard G.992.5 January 2003
  Speed Downstream/Upstream 24/2 Mbps
Other Major Enhancements
  Diagnostics
  Power enhancements
  Rate adaptation
  Bonding for higher data rates
  Channelization and Channelized Voice-over DSL (CVoDSL)
Additional Benefits
  Improved interoperability
  Fast startup
  All-Digital Mode
  Support of packet-based services
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 63: ADSL2 Rate and Reach
  Notes
Data rate increase of 50 kbps or increase of 600 feet reach achieved
Programmable overhead
  ADSL 32 kbps
  ADSL2 4-32 kbps
Higher coding gain from Reed-Solomon (RS) code
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 64: ADSL2 Power Enhancement
  Notes
Savings in ATU-C and ATU-R
L0 Full power
L2 Normal power
L3 Sleep mode (user not on line)
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 65: Seamless Rate Adaptation
  Notes
Telephone cable in bundle of 25 or more
Next and Fext can cause connection drop
SRA (Seamless Rate Adaptation) decouples modulation and framing layers
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 66: Bonding for Higher Data Rates
  Notes
Bonds two or more UTP using ATM IMA (Inverse Multiplexing for ATM)
New sublayer between PHY and ATM
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 67: Other ADSL2 Enhancements
  Notes
Diagnostics by use of enhanced transreceivers
  Line noise
  Loop attenuation
  SNR (Signal-to-Noise ratio)
Improved interoperability due to initialization of state machine
Fast startup
Transmission of ADSL data in the voice bandwidth
Ethernet over ADSL2
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 68: Basic ADSL Management Model
  Notes
Supports a simple and fixed channel
  Fast channel
  Interleaved channel or
  Both
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 69: Multichannel DSL Management
  Notes
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Decouple channel parameters from line parameters
Up to four generic channels
Flexible configuration
Many combinations of parameters to manage

## Slide 70: Passive Optical Network
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 71: Passive Optical Network
  Notes
Fiber Medium
No active elements in the transmission medium
Passive elements in the fiber medium
  Beam splitter – Lossy
  Wavelength Division Multiplexer (WDM)
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 72: Generic PON Architecture
  Notes
Optical Line Termination (OLT) in central office
Optical Network Unit (ONU) in customer residence
Shared or dedicated optical path
1-way and 2-way transmission using separate physical or optical wavelength (λ) path
Dedicated fiber (λ) vs. shared medium multiple (λ)
3 deployment configurations
  Dedicated fiber
  EPON
  WDM
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 73: PON Configurations: Dedicated Fiber
  Notes
Dedicated fiber from OLT to each ONU
ONU function similar to ONU in cable access network
One-way in each fiber / Dual wavelength fiber for 2-way
Expensive configuration
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Figure 13.31(a) PON Configuration (Point-to Point PON)

## Slide 74: PON Configuration: EPON
  Notes
Shared optical fiber from OLT to power splitter / combiner
Twisted pair or Cat-x cable from splitter / combiner to ONU
Modified Ethernet MAC protocol for EFM (Ethernet First Mile)
Downstream TDM and upstream TDMA
MIB specified only for EPON
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Figure 13.31(b) PON Configuration (EPON)

## Slide 75: PON Configuration: WPON
  Notes
Shared single fiber from OLT to WDM
Multiple (λ), one to each ONU
DWDM (Dense WDM) special case of WDM
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Figure 13.31(c) PON Configuration (WPON)

## Slide 76: EPON MAC Protocol
  Notes
Point-to-Multipoint architecture
OLT with n virtual ports communicates with n ONUs
Communication established through virtual tunneling
Different from IP/SNMP used for traditional 802.3 -> 802.3ah
Some management capabilities are embedded in Ethernet layer
802.3ah defines both physical and MAC layer
Modified gigabit Ethernet protocol
PON link based on shared optical fiber with optical splitter dividing the subscribers
Multipoint control protocol embedded in MAC layer to control EPON subscribers
Emulation layer creates virtual private path to each ONU
FEC error correction
802.1d – modified bridge – in the MAC layer sets up peer-to-peer communication between OLT and ONU
Management layer embedded in MAC layer for OAM
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 77: EPON Protocol Architecture
  Notes
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 78: Managed EPON Protocol Architecture
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 79: EPON MIB
  Notes
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 80: EPON Group
  Notes
Entity | OID | Description (brief)
dot3EponMIB | Mib-2 155 | EPON MAC
dot3EponObjects | dot3EponMIB 1 | EPON MIB objects
dot3MpcpObjects | dot3EponMIB 1 | 802.3ah MPCP attributes
dot3EmulationObjects | dot3EponMIB 2 | Point-to-point OMP emulation attributes
dot3EponFecObjects | dot3EponMIB 3 | EPON FEC attributes
dot3ExtPkgObjects | dot3EponMIB 4 | Configuration and status attributes of Extended EPON
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Table 13.16 EPON Group

## Slide 81: ONU Interface MIB Example
  Notes
Table 13.17 ONU Interface MIB Example
Interface MIB Object | Optical Interface Value | ONU Interface Value
ifIndex | 1 | 100
ifDescr | “Interface Description” | “Interface Description”
ifType | ethernetCsmacd (6) 1000base-Px | ethernetCsmacd (6) 1000base-Px
ifMtu | MTU size (1522) | MTU size (1522)
ifSpeed | 1000000000 | 1000000000
ifPhysAddress | ONU_MAC_Address | ONU_MAC_Address
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 82: OLT Interface MIB Example
  Notes
Table 13.16 OLT Interface MIB Example
Interface MIB Object | Optical Interface Value | ONU Interface Value | ONU Interface Value | ONU Broadcast Interface Value
ifIndex | 2 | 200001 | 200002 | 265535
ifDescr | “Interface Description” | “Interface Description” | “Interface Description” | “Interface Description”
ifType | ethernetCsmacd (6) 1000base-Px | ethernetCsmacd (6) 1000base-Px | ethernetCsmacd (6) 1000base-Px | ethernetCsmacd (6) 1000base-Px
ifMtu | MTU size (1522) | MTU size (1522) | MTU size (1522) | MTU size (1522)
ifSpeed | 1000000000 | 1000000000 | 1000000000 | 1000000000
ifPhysAddress | OLT_MAC_Address | OLT_MAC_Address | OLT_MAC_Address | OLT_MAC_Address
Table 13.16 OLT Interface MIB Example
Interface MIB Object | Optical Interface Value | ONU Interface Value | ONU Interface Value | ONU Broadcast Interface Value
ifIndex | 2 | 200001 | 200002 | 265535
ifDescr | “Interface Description” | “Interface Description” | “Interface Description” | “Interface Description”
ifType | ethernetCsmacd (6) 1000base-Px | ethernetCsmacd (6) 1000base-Px | ethernetCsmacd (6) 1000base-Px | ethernetCsmacd (6) 1000base-Px
ifMtu | MTU size (1522) | MTU size (1522) | MTU size (1522) | MTU size (1522)
ifSpeed | 1000000000 | 1000000000 | 1000000000 | 1000000000
ifPhysAddress | OLT_MAC_Address | OLT_MAC_Address | OLT_MAC_Address | OLT_MAC_Address
Interface MIB Object | Optical Interface Value | ONU Interface Value | ONU Interface Value | ONU Broadcast Interface Value
ifIndex | 2 | 200001 | 200002 | 265535
ifDescr | “Interface Description” | “Interface Description” | “Interface Description” | “Interface Description”
ifType | ethernetCsmacd (6) 1000base-Px | ethernetCsmacd (6) 1000base-Px | ethernetCsmacd (6) 1000base-Px | ethernetCsmacd (6) 1000base-Px
ifMtu | MTU size (1522) | MTU size (1522) | MTU size (1522) | MTU size (1522)
ifSpeed | 1000000000 | 1000000000 | 1000000000 | 1000000000
ifPhysAddress | OLT_MAC_Address | OLT_MAC_Address | OLT_MAC_Address | OLT_MAC_Address
Chapter 13 Broadband Network Management: Wired and Optical Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Table 13.18 ONU Interface MIB Example