## Slide 1: Chapter 14 Broadband Wireless Access Networks
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 2: Objectives
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Broadband wireless access networks
  Multichannel multipoint distribution service, MMDS
  Local multipoint distribution service, LMDS
  IEEE 802.16/WiMax networks
Components of wireless access network
  Base station (BS)
  Subscriber station (SS)
  Wireless medium
  Wireless spectrum
Basic principles of wireless communication
  Free space propagation
  Terrestrial propagation
  Cellular mobile environment
  Fading phenomena
MMDS and LMDS
  Deployment in rural areas
  Line-of-sight (LOS) limitation
  Operational spectrum and modes
  Similarity with cable access network
  DOCSIS standards or proprietary protocol
  DOCSIS management standards for DOCSIS-based systems
*
Notes: Chapter 14

## Slide 3: Objectives (cont.)
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
IEEE 802.16/WiMax networks
  IEEE 802.16 spectrum 10 to 66 GHz
  WiMax spectrum windows in the 2 to 11 GHz
  WiMax mesh network eliminates LOS limitation
  Management of BS and SS
  Spectrum management
  Service flow management
  Management using wmanIfMib
Mobile wireless network
  2.5, 3, and 4G technologies
  TDM, TDMA, and CDMA protocol systems
  Management issues
  Use of mobile IP
  Mobility management
  Power and resource management
  QoS management
  Security management
VSAT network and management
*
Notes: Chapter 14

## Slide 4: Wired & Wireless Broadband Networks
  Notes
Wireless Mobile ATM (WmATM) is not shown in Wireless WAN as it does not appear to be in the current road map of technology.
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 5: Wireless Broadband Networks
  Notes
Access Networks
  MAN a.k.a. WiMax
Wireless LAN (WLAN)
Personal Area Network (PAN)
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 6: Basic Principles
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 7: Outdoor Propagation
  Notes
Adverse Characteristics:
  Attenuation
  Dispersion: Frequency and Phase (independent of refractive index)
  Dispersion due to refractive index
  Decreasing signal strength due to beam pattern
  Water absorption
  Fading: short and long
  Doppler effect
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 8: Isotropic Propagation
  Notes
Pr = (PT / 4πd2) watts /m2 (14-1)
Pr = Received power per unit area and
PT = Total transmitted power.
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 9: Non-Isotropic Propagation
  Notes
PR = PTGTGR (λ / 4d)2 (14-5)
PR = Received power
PT = Transmitted power
GT = Transmitter antenna gain
GR = Receiver antenna gain
λ = Wavelength
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 10: Satellite Free Space Propagation
  Notes
PR ά 1/d2
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 11: Terrestrial Propagation
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
  Notes
PR ά 1/d2
Notes: Chapter 14

## Slide 12: Path Loss Dependency
  Notes
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 13: Shadow Fading
  Notes
Large-scale fading
  Slow spatial rate compared to wavelength
  Slow rate of change
Small-scale fading or Shadow fading
  Spatial dimension comparable to wavelength
  Rapid rate of change
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 14: Fixed Wireless Networks
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 15: Fixed Wireless Network
  Notes
Fixed wireless access
  a.k.a wireless local loop
Point-to-multipoint network architecture
Benefits:
  Less capital investment
  Quick and cheap to install and operate
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Figure 14.9 Fixed Wireless Access Network
*

## Slide 16: MMDS
  Notes
Point-to-multipoint architecture
Range between BSs is 50 km
Operates over 2.5 to 2.686 GHz band
Could operate on multichannels and hence capable of providing 2-way high-speed communication
An implementation using cable modem equipment at both ends
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 17: LMDS
  Notes
Point-to-multipoint architecture
Covers 5 km radius; BSUs spaced 10 km apart
Operates over 27-28.35 and 31-31.3 GHz bands
Sensitive to rain attenuation
Deploys cable modem equipment at both ends
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 18: MMDS and Cable Network Management
  Notes
MMDS managed using DOCSIS (Data-Over- Cable Standard Interface Specifications)
Head end:
  Signals from multiple sources multiplexed
  Frequency conversion for local signal
NIU demarcation point between customer and service provider networks
Cable modem: RF-to-Ethernet conversion
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 19: MMDS / LMDS Network Management
  Notes
Head end is replaced by base station
Cable modem replaced by transceiver and subscriber station
HFC plant replaced by wireless
DOCSIS standards used for the system
DOCSIS management standards adapted for management
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 20: 802.16 Fixed Wireless System
  Notes
IEEE 802.16.1 specifications for 11 GHz to 66 GHz @ 2 to 155 Mbps with flexible asymmetry
Encompasses multiple end configurations and transmission modes
Point-to-multipoint architecture
Early implementation based on cable network
HFC medium replaced with wireless carrier
Transceivers perform up-conversion and down-conversion
Subscriber station a more complex modem than CM
Base station functions as enhanced CMTS
TDMA (Time Division Multiple Access) downstream transmission
DAMA (Demand Assigned Multiple Access) – TDMA upstream transmission
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Figure 14.13 IEEE 802.16 Fixed Wireless System
*

## Slide 21: 802.16 Base Station
  Notes
802.16 uses sector technology for base station antenna (HFC uses tree topology)
Point-to-multipoint transmission
All SSs in a cell terminated at the head end
Downstream in broadcast mode
Upstream transmission by DAMA-TDMA
Allocates bandwidth requested by SS to meet QoS
Gateway to the external (core) network
Multiplexes and demultiplexes signals
Frequency converts upstream to downstream signals in FDD (Frequency Division Duplex)
Can be designed either as a bridge or router
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 22: 802.16 Subscriber Station
  Notes
Highly directional antenna
DOCSIS 1.1 (and beyond) compliant CM used with primary upstream service flow
Downstream in broadcast mode
Upstream transmission by CM/SS coordinated by head end
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 23: IEEE 802.16 Extensions
  Notes
IEEE 802.16a
  2 to 11 GHz; Supports mesh deployment
IEEE 802.16b
  5 TO 6 GHz; Real-time DiffServ service
IEEE 802.16c
  10 to 66 GHz
IEEE 802.16d
  Improvement over 802.16a
IEEE 802.16e (future)
  Std networking between carrier base stations
  High-speed handoff with moving vehicles
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 24: 802.16d WiMax
  Notes
WMAN … Wireless Metropolitan Network
802.16a can support no-line-of-sight access
(unlike 802.16)
802.16a operated in the frequency range of 2 – 11 GHz and thus supports both licensed and unlicensed spectrum
Modulation scheme is OFDM as in 802.11a and 802.11g
Support for mesh architecture.
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Figure 14.14 WiMax Mesh Network
*

## Slide 25: 802.16d: PHY Layer
  Notes
Air interfaceWirelessMAN-
  SCa Single carrier
  OFDM (commonly adopted) 256-carrier OFDM TDMA upstream
  OFDMA 2048-carrier OFDM Upstream OFDMA – multiple carriers assigned to a receiver
Modulation and decoding
  QPSK
  16-QAM
  64-QAM
Adaptive antenna system
  Directed beams in PMP (Point-to-Multipoint)
  Channel quality feedback from SS to BS
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 26: 802.16d: MAC Layer
  Notes
Supports mesh network
Two sublayers
  Convergence-specific: transport-specific
  Common: independent of transport mechanism
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 27: Fixed BWA (Broadband Wireless Access) Management
  Notes
Components to be managed:
  CM/SS management
  BS management
  Wireless link management
  RF spectrum management
802.16 Recommendation OSI standards
FCAPS functions managed
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 28: Class of Service and QoS
  Notes
802.16.1 supports classes of service with various QoS for bearer services
Bandwidth negotiation for connectionless service
State information maintainable for connection- oriented service
ATM Traffic categories:
  CBR, VBR-rt, VBR-nrt, ABR, ABR
IETF Traffic categories: (Integrated services RFC 1633 and differentiated services RFC 2475)
  Elastic:
    Interactive bursts (Telnet)
    Interactive bulk (FTP)
    Asynchronous bulk (email)
  Real-time
    Guaranteed service (audio and video conferencing)
    Predictive service (video playback)
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 29: BWA NM Reference Model
  Notes
Reference: “MAC and PHY MIB for WirelessMAN and WirelessHUMAN BS and SS,” IEEE C802.16mgt-04/04r1, http://ieee802.org/16
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Figure 14.15 BWA Network Management Reference Model

## Slide 30: WMAN IF MIB
  Notes
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Figure 14.16 WMAN IF MIB

## Slide 31: Usage of ifTable Objects for Base Station
  Notes
SNMP agent in a common base station controller: Each BS sector will have an entry in the ifTable
SNMP agent in the sector controller: One entry for the BS sector in the ifTable
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Table 14.1 Usage of ifTable Objects for the Base Station

## Slide 32: Usage of ifTable Objects for Subscriber Station
  Notes
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Table 14.2 Usage of ifTable Objects for the Subscriber Station

## Slide 33: Commercial Examples
  Notes
CorDect / CorVan
Ricochet
Broadband Solutions
MeshNetworks
PacketHop
Navini
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 34: DECT WLL
  Notes
Digital European Cordless Telecommunications
Digital Enhanced Cordless Telecommunications
Frequency spectrum
  ISM 2.4 GHz
  DECT 1.9 GHz
Low-cost DCT design platforms for base stations and handsets
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 35: corDect
  Notes
Midas Communications / IITM TeNet Group
Components
  Central station: DIU
  Base Stations: 5 BSDs per DIU
  Air Interface: 4 CVSs per BSD
Simultaneous voice and dedicated Internet access (up to 70 Kbps)
Coverage up to 10 km, can be extended to 35 km using relay base station
EMS / NMS with proprietary MIB
.
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 36: Ricochet Internet Access
  Notes
Source: IEEE Spectrum, March 2002
128 kbps Internet connection
Unlicensed 900 MHz spectrum
Access Points mounted on light poles
Established in 22 cities
Filed bankruptcy in 2001
Bought out by Aerie Networks
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 37: BBSC Broadband Solution
  Notes
Broadband Solutions Co. (BBSC) broadband net- work in Utah uses fixed wireless access network
Has 6 wireless hubs over 1500 square kilometers
Supports 1400 customers
Supports hot spots of 2 – mbps connectivity
Operation at 2.4 and 5.7 GHz
Broadband Solutions Co. (BBSC) Hub
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 38: MeshNetworks Enabled Architecture
  Notes
Supports
  Backhaul access point infrastructure
  Client meshing of wireless peer-to-peer networks
Supports handoff between access points from mobile auto
Test set-up in Florida supports 500 kbps in moving vehicle at highway speed
Source: www.MeshNetworks.com
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 39: PacketHop
  Notes
Source: www.packethop.com
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 40: PacketHop Technology
  Notes
Mobile units act as routers in a mesh configuration
Source: www.packethop.com
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 41: Navini Ripwave
  Notes
Fixed wireless
Components
  Base Station
  Element Management System
  Modem
Operates in the unlicensed 2.4 GHz ISM band, or the licensed 2.3 GHz WCS, 2.5/2.6 GHz ITFS/MMDS bands
Source:www.navini.com
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 42: Mobile Wireless Networks
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 43: Mobile and Wireless
  Notes
Mobile Network
  A network with ability to perform computing anytime/anywhere
  May or may not use wireless transmission medium
  Types of mobility
    Cellular: Always-on
    Nomadic: Session not active while in motion
Wireless Network
  A network with wireless interface to computing devices and/or wired network
  Deployed for networking both fixed and mobile users
Mobile and Wireless Broadband Network Management
  Management of integrated wired/wireless and fixed/mobile broadband – voice, video, and data networks
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 44: Mobile Wireless Evolution
  Notes
IS-136/DAMPS TDMA-based
GSM TDMA-based
IS-95 CDMA based
FDD (Frequency Division Duplex)
  IS-136, GSM/GPRS, and IS-95
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 45: Cellular Network
  Notes
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Table 14.17 Cellular Network
Notes: Chapter 14

## Slide 46: 3G Management Issues
  Notes
Hierarchical LAN
Joint management with wired network
Mobile computing unit
  Hardware limitations
  Software limitations
Mobility management
Location tracking
Resource management
Wireless QoS management
Power management
Security management
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 47: Mobility Management
  Notes
Mobile IP
Location tracking
  Discovery of Foreign Agents by Mobile Units
  Broadcasting/advertising to locate an MU
  Solicitation by MU
Handoff management
  Packet control function (PCF) / Radio Network
  Handoff of PCF to PCF within PDSN
  Handoff of PCF between PDSNs
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 48: Mobile IP
  Notes
Mobile vs. nomadic
  Mobile: activities not disrupted when point of attachment is changed
  Nomadic: not active in motion; a.k.a. Portable computing
Analogy with telephone: Subscriber assigned an ID in both – phone number vs. IP address
Mobile IP is analogous to call forwarding, except the forwarding address is mobile
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 49: Mobile IP Functions - Roaming
  Notes
Mobile IP uses two addresses: a fixed home address and a care-of-address that changes the point of attachment
Mobile IP functions:
  Mobile Agent ( Mobile Node) Discovery of foreign agent (FA)
  Registration of current location with FA and home agent (HA)
  Tunneling of packets to and from the HA to FA care-of-address as mobile node roams
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 50: Discovery and Registration
  Notes
  Mobile node discovers foreign agent (FA) and its care-of-address by advertisements of FA
  Mobile node can also discover by its solicitation
  Mobile node registers FA with HA
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Table 14.18 Discovery and Registration in a Mobile System
Notes: Chapter 14

## Slide 51: Tunneling
  Notes
Protocol number in the header:
  4 indicates to higher level that the next header is an IP header with full encapsulation
  55 indicates minimal encapsulation
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Table 14.19 Tunneling in a Mobile System
Notes: Chapter 14

## Slide 52: SNMP Management of Mobile IP
  Notes
IETF Specifications using SMIv2 (RFC 1902) and MIB-II (RFC 1213)
Functional entities:
  Mobile Node: A host or router that changes point of attachment from one network or subnet to another
  Home Agent: A router on a mobile node’s home network, which tunnels packets to and from the mobile node via foreign agent
  Foreign Agent: A router on a mobile node’s visited network, which provides services to the mobile node
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 53: Mobile IP MIB Groups
Groups | Mobile Node | Foreign Agent | Home Agent
mipSystemGroup | X | X | X
mipSecAssociationGroup | X | X | X
mipSecViolationGroup | X | X | X
mnSystemGroup | X |  | 
mnDiscoveryGroup | X |  | 
mnRegistrationGroup | X |  | 
maAdvertisementGroup |  | X | X
faSystemGroup |  | X | 
faAdvertisementGroup |  | X | 
faRegistrationGroup |  | X | 
haRegistrationGroup |  |  | X
haRegNodeCountersGroup |  |  | x
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 54: Mobile IP MIB
  Notes
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Figure 14.20 Mobile IP MIB
Notes: Chapter 14

## Slide 55: mipMIBObjects
  Notes
Entity | OID | Description
mipMIBObjects | mipMIB 1 | Objects under mipMIB
mipSystem | mipMIBObjects 1 | Mobile IP system related parameters
mipSecurity | mipMIBObjects 2 | Mobile IP security parameters
mipSecurity AssociationTable | mipSecurity 1 | Security associations table
mipSecTotal Violations | mipSecurity 2 | Total number of security violations in the entity
mipSecViolation Table | mipSecurity 3 | Security violation information
mipMN | mipMIBObjects 3 | Mobile node group
mnSystem | mipMN 1 | Mobile node system information
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Table 14.4 mipMIBObjects
Notes: Chapter 14

## Slide 56: mipMIBObjects
Entity | OID | Description
mnDiscovery | mipMN 2 | Mobile node discovery counter on solicitations, advertisements, and moves
mnRegistration | mipMN 3 | Mobile node registration table
mipMA | mipMIBObjects 4 | Mobile agent group
maAdvertisement | mipMA 1 | Mobility agent advertisement configuration table present in both MN and FA
mipFA | mipMIBObjects 5 | Foreign agent group
faSystem | mipFA 1 | Foreign agent system information
faAdvertisement | mipFA 2 | Foreign agent advertisement information plus MA advertisement group
faRegistration | mipFA 3 | Foreign agent visitors list
mipHA | mipMIBObjects 6 | Home agent registration group and mobility binding list
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Table 14.4 mipMIBObjects (cont.)
Notes: Chapter 14

## Slide 57: Resource Management
  Notes
Scheduling and call admission control
  Reservation of guard channels for handoff - static
  Dynamic control of call admission – complex to control multimedia service
  Proposals for QoS-based handoffs
Load balancing between access networks
Power management
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 58: Security Management
  Notes
WAP (Wireless Application Protocol) Security
  WAP Wireless transport layer security (WTLS)
    Based on transport layer security (TLS) or secured sockets shell (SSL)
    “Walled garden” “vertical” integrated approach
3G network security
  3GPP (Third Generation Partnership Project) and 3GPP2 plan for IP to wireless device
  Open standard SNMP based
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 59: QoS Management
QoS support for last leg between access point and mobile node
Depends on mobility and resource management
3GPP/3GPP2 (3G Partnership Project) standards ensure interoperability
3GPP has defined four QoS classes (TS 23.107) shown above
Telephony handled using SIP (session initiation protocol)
Backbone based on DiffServ
QoS Class | TransferDelay | Transfer Delay Variation | Low BER | Guaran-teed Bit Rate | Example
Conver-sation | Strin- gent | Strin- gent | No | Yes | VoIP, Video- and Audio-conferencing
Stream-ing | Con- strained | Con- strained | No | Yes | Broadcast service, news, sport
Inter- active | Looser | No | Yes | No | Web browsing, interactive chat, games
Back-ground | No | No | Yes | No | email, SMS, TFP transactions
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Table 14.5 UMTS QoS Specifications
  Notes
Notes: Chapter 14

## Slide 60: VSAT
  Notes
KU Band and KA band
40 – 60 kbps uplink and 500 kbps downlink
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14

## Slide 61: VSAT Components
  Notes
ODU Outdoor unit
  Power amplifier
  Up-converter
  Down-converter
IDU Indoor unit
  Modems
  Frequency synthesizer
  Encoder / decoder
Proxy agent for management; Later models with SNMP agent
Chapter 14 Broadband Wireless Access Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
*
Notes: Chapter 14