## Slide 1
Chapter 6
SNMP Management : SNMPv2
Last modified: 24/02/2018
Chapter 6 SNMP Management : SNMPv2

## Slide 2
Objectives
SNMPv2 enhancements
  Additional messages
  Formalization of SMI
SNMPv2 System Architecture
SNMP MIB modifications
Table expansion
SNMP v2 PDUs and operations
Compatibility with SNMPv1
  Proxy server
  Bilingual manager
Chapter 6 SNMP Management : SNMPv2

## Slide 3
Major Changes (1/2)
Two new messages :
  1. Bulk data transfer message: speeds up get-next-request
    Useful to retrieve data from tables
  2. Manager-to-manager message: deals with interoperability
Enhancements to SMI: SMIv2 has 3 parts
  Module definitions: MODULE-IDENTITY macro- Defines the semantics of information module
  Object definitions: OBJECT-TYPE macro –Defines the syntax and semantics of managed objects
  Trap definitions: NOTIFICATION-TYPE macro –Defines the notifications
Chapter 6 SNMP Management : SNMPv2

## Slide 4
Chapter 6 SNMP Management : SNMPv2
Textual conventions – defines new data types
Conformance statements – helps the customers to compare various products, and the vendors to be honest in claiming their product to be compatible with SNMP version.
Row creation and deletion in table
MIB enhancements
  Internet node has 2 new subgroups: security and snmpv2
Change in communication model – Transport mappings- other than UDP at transport layer –
Security features, originally to be in SNMPv2 moved to SNMPv3
SNMPv2, like SNMPv1, is community-based administrative framework
.
Major Changes (2/2)

## Slide 5
MIB enhancements
  Notes
Some new Objects are added to System group in SNMPv2 MIB
Extensive modification is done in SNMP group
Additional SNMPv2 group added
The entities in SNMPv2 are hybrid, with some from SNMPv1 and some added under SNMPv2 node
Security group is a placeholder – has no objects
Chapter 6 SNMP Management : SNMPv2

## Slide 6
SNMPv2 NM Architecture
  Notes
Compare this figure with figure 4.9- SNMPv1 architecture
Chapter 6 SNMP Management : SNMPv2

## Slide 7
SNMPv2 New Messages
inform-request
  manager-to-manager message
get-bulk-request
  transfer of large data
report
  not used
  It is not specified  It is left to vendors
Chapter 6 SNMP Management : SNMPv2

## Slide 8
Structure of Management information v2 (SMIv2)
  Notes
Module is a group of related assignments
MODULE-IDENTITY macro defines the module definitions. It provides administrative info and revision history
In the example MODULE – IDENTITY macro, (for a network component vendor ‘isi’ Info Tech Service) all clauses except the Revision clause is mandatory
Chapter 6 SNMP Management : SNMPv2

## Slide 9
OBJECT DEFINITIONS
Object Identity macro defines information about an object identifier
OBJECT IDENTIFIER defines the administrative identification of a node in the MIB
OBJECT-IDENTITY macro assigns an object identifier to an object identifier in the MIB
OBJECT-TYPE macro defines the type of a managed object. It is also used to describe a new type
Chapter 6 SNMP Management : SNMPv2

## Slide 10
OBJECT-IDENTITY / OBJECT-TYPE
OBJECT-IDENTITY is high level description
OBJECT-TYPE details description needed for implementation
Chapter 6 SNMP Management : SNMPv2

## Slide 11
Table Expansion
  Notes
  Table expansion is done when the number of columnar objects needs to be increased, or when the objects are best organized by grouping them hierarchically
  3 restrictions: (a) the number of conceptual rows is not affected by the addition; (b) there is one-to-one correspondence between the rows of the two tables; and (c) the INDEX of the second table is the same as that of the first table
Augmentation of a table (dependent table) adds additional columns to an
existing table (base table)
Dense table enables addition of more rows to base table
Sparse table supplements less rows to a base table
Chapter 6 SNMP Management : SNMPv2

## Slide 12
Augmentation of Tables
Notes
Table 1 & 2 are aggregate objects
Table1: called base table; Table2: augmented table
Table 1 has 4 rows and 3 columns-base table
Table 2 has 4 rows and 2 columns-augmented table
There is a one-to-one correspondence in rows between the two tables
After combining the table, it still has 4 rows
Chapter 6 SNMP Management : SNMPv2

## Slide 13
Augmentation of Tables: Example
Notes
IpAddrTable is the base table
ipAugAddrTable is the augmented table
ipAugAddrTable could add two more columnar objects defining the board and port number associated with the ipAdEntIfIndex.
Chapter 6 SNMP Management : SNMPv2

## Slide 14
Textual Convention
Enables defining new data types
Makes semantics of data types consistent and human readable
Creates new data types using existing ones and applies restrictions to them
An important textual convention in SNMPv2, RowStatus -creates and deletes rows
SNMPv2:
SNMPV1:
  Notes
Textual convention is defined as a data-type in SNMPv2
It gives the syntax and meaning of the textual convention
Display-hint gives more information about the value of instance of the object. For example here, ‘a ‘ represents ASCII, we can have b – binary O – octal etc. SNMPV1 has no such option
Example
Chapter 6 SNMP Management : SNMPv2

## Slide 15
Creation of Row: RowStatus
  Notes
Status: A new column is added to the conceptual table
SYNTAX of Status is RowStatus
Value of RowStatus is Enumerated INTEGER
Last 3 states , along with first state are used by the manager to create and delete rows
First 3 states are used by the agent to give response to the manager
Chapter 6 SNMP Management : SNMPv2

## Slide 16
Row Creation and Deletion
Chapter 6 SNMP Management : SNMPv2

## Slide 17
Create-and-Go Row Creation
Notes
The manager sends a request to the agent to create a row and make it active immediately, by setting status = 4
Index represents the row number. Index is suffixed with the other two columnar objects also
Here we are adding a row in the third position.
The default value of DefData is data 3
Now the agent creates the row by interacting with the managed entity
Status = 1 in the response, i.e. row is active.
The response also contains the values of all columnar objects
Chapter 6 SNMP Management : SNMPv2

## Slide 18
Create-and-Wait: Row Creation (1/2)
Chapter 6 SNMP Management : SNMPv2

## Slide 19
Notes
The Manager sends a SetRequest PDU with status 5, to mean create a row and wait
Since a value for the columnar object is not passed by the manager, the agent sends a response with status 3, which means the row is NotReady
The manager now sends a GetRequest message asking for data in the 3rd row
The agent responds with saying “NoSuchName” because there is no value yet
The manager sends SetRequest for setting value DefData
The agent responds, the row is NotInService
Now the manager sends SetRequest with status as 1 = Active. The agent responds (confirms) with status 1
Note that every time the manager sends a request, the agent either validates or sets the value
Create-and-Wait: Row Creation (2/2)
Chapter 6 SNMP Management : SNMPv2

## Slide 20
Row Deletion
Notes
For deleting a row, the manager sends SetRequest
With status 6, to destroy a specific row
Independently of the status of the row, it is deleted by the agent and a response is sent back
Chapter 6 SNMP Management : SNMPv2

## Slide 21
SNMPv2 MIB
  Notes
Security is a placeholder
System group: A table sysORTable added that lists resources that the agent controls; NMS configures NE through the agents.
Most of the objects in the SNMPv1 obsoleted
Object Groups and Notification Groups defined for conformance specifications.
Chapter 6 SNMP Management : SNMPv2

## Slide 22
Conformance: OBJECT-GROUP
  Notes
Conformance defined by
  OBJECT-GROUP macro
  NOTIFICATION-GROUP macro
OBJECT-GROUP
  Compiled during implementation, not at run time
  OBJECTS clause names each object
  Every object belongs to an OBJECT-GROUP
  Access defined by MAX-ACCESS, the maximum access privilege for the object
Chapter 6 SNMP Management : SNMPv2

## Slide 23
Conformance: NOTIFICATION-GROUP
  Notes
NOTIFICATION-GROUP
  Contains trap entities defined in SMIv1
  NOTIFICATIONS clause identifies the notifications in the group
  NOTIFICATIONS-GROUP macro compiled during implementation, not at run time
Chapter 6 SNMP Management : SNMPv2

## Slide 24
Compliance-module compliance
  Notes
Compliance has two classes of groups
  MANDATORY-GROUPS ... Required
  GROUP …Optional
  Module compliance macro defines minimum set of requirements for implementation of one or more MIB modules.
Chapter 6 SNMP Management : SNMPv2

## Slide 25
Agent Capabilities
AGENT-CAPABILITIES - statements are used by manufacturers and implementers of SNMP agents to document (for their users) the features supported by the implementation.
AGENT-CAPABILITIES macro
  SUPPORTS modules and includes groups
  VARIATION identifies additional features
  Notes
The actual MIB modules that are implemented in an agent are specified by module Agent Capabilities
Objects and notifications are combined into groups for the convenience of defining module compliance and agent capabilities
Chapter 6 SNMP Management : SNMPv2

## Slide 26
SNMPv2 SNMP MIB
Compare this to SNMPv1 MIB!
Notes
The SNMP group in SNMPv2 is simplified by removing many entities.
It has just 8 entities, 6 from old ( 1,3,6,30,31,32) and 2 newly added (4,5)
Chapter 6 SNMP Management : SNMPv2

## Slide 27
snmpMIBObjects MIB
Chapter 6 SNMP Management : SNMPv2

## Slide 28
Notes
The information on Trap is redefined in SNMPv2 and added under snmpMIBObjects
Three modules under snmpMIBObjects
  snmpTrap(4) – information group containing trapid and enterprise id
  snmpTraps(5) – well known traps
    Not the same OID! in SNMPv1, coldStart has OID 0, WarmStart = 1, etc.
  snmpSet(6) – manager to manager -Notification message
Subnodes 1,2,3 are obsolete
snmpMIBObjects MIB continued
Chapter 6 SNMP Management : SNMPv2

## Slide 29
SNMPv2 PDU
  Notes
PDU type – identifies the PDU type out of 7 messages
RequestID uniquely identifies the request response pair
Error status and error index are used to identify error in communication if any
  In request messages from the manager, these two fields are either set to 0 or ignored
  In the response message, (from the agent) error status is set to 0 if no error, otherwise corresponding status value and index are entered
  There is a list of error status, shown in next slide. Error index identifies the variable binding in the variable binding list, which caused the error
The variable binding list is the list of varbind name and value for which the manager requested values
Standardized format for all messages
Interpretation of error status and error index fields; In v1, if error occurs status and index field filled, but varBindList blank
Chapter 6 SNMP Management : SNMPv2
Interpretation in v2 Status Index
varBindList ignored x
varBind of index field ignored x x

## Slide 30
SNMPv2 PDU and Error Status
Chapter 6 SNMP Management : SNMPv2

## Slide 31
SNMPv2 GetBulkRequest PDU
  Notes
Error status field replaced by Non-repeaters
Error index field replaced by Max repetitions
No one-to-one relationship between request and response
  Because the response will be larger than the request
Non-repeaters: number of non-repetitive scalar values
Max Repetitions: maximum number of tables rows
Chapter 6 SNMP Management : SNMPv2

## Slide 32
Get-Bulk-Request: Generic MIB
Chapter 6 SNMP Management : SNMPv2

## Slide 33
Get-Next-Request Operation
  Notes
If it continues the operation, it would receive a noSuchName error message
Chapter 6 SNMP Management : SNMPv2

## Slide 34
Get-Bulk-Request Operation
Chapter 6 SNMP Management : SNMPv2

## Slide 35
Notes
The entire MIB can be read in just two requests and responses
The first request says, retrieve 2 non repetitive objects (the first value 2  requesting A and B) and 3 repetitive objects (second operand 3  of the columnar object T.E.1, T.E.2, T.E.3)
The response yields value of A and B for the non repetitive objects and first 3 rows of the aggregate object
The second request is for three more rows of the table
Since there is only one row left to retrieve, the agent responds with the last row, the next lexicographic entity z, and error message “endOfMIBView”
  The manager understands it as the end of the table
Get-Bulk-Request Operation continued
Chapter 6 SNMP Management : SNMPv2

## Slide 36
Get-Bulk-Request Example
Chapter 6 SNMP Management : SNMPv2

## Slide 37
SNMPv2 Trap
  Notes
Addition of NOTIFICATION-TYPE macro
OBJECTS clause, if present, defines order of variable bindings
Positions 1 and 2 in VarBindList are sysUpTime and snmpTrapOID
Chapter 6 SNMP Management : SNMPv2

## Slide 38
Inform-Request
  Notes
Inform-Request behaves as trap in that the message goes from one manager to another unsolicited
The receiving manager sends response to the sending manager
  Recall that a trap is passively received by a manager
Chapter 6 SNMP Management : SNMPv2

## Slide 39
Compatibility with SNMPv1: Bilingual Manager
  Notes
Compatibility with SNMPv1 can be achieved in two ways
  Bilingual Manager
  Proxy Server
Bilingual Manager: Implements both snmpv1 and v2 interpreter modules. The interpreter does all conversions and functions needed
  Conversion of MIB variables and SNMP protocol operations in both directions
The SNMP PDU contains the version number field
Disadvantage: expensive in resource and operation
Chapter 6 SNMP Management : SNMPv2

## Slide 40
Compatibility with SNMPv1: SNMP Proxy Server (1/2)
Chapter 6 SNMP Management : SNMPv2

## Slide 41
Notes
SNMPv2 messages are passed without any changes
SNMPv1 messages are sent to the manager through the proxy
The GetRequest, GetNextRequest, and SetRequest PDUs from SNMPv2 manager are passed though the proxy server without any change
There are two modifications applied to GetBulkRequest PDU, the values of the two fields non-repeaters and max-repetitions to 0, and transmitted as GetNextRequest
The GetResponse from v1 is passed through proxy unaltered, unless a response has tooBigError value
  In the tooBigError case the variable binding field should be removed
The Trap from SNMPv1 agent is prepended with two varBind fields, sysUptime 0, and snmpTrapOID 0, with their associated values and then passed on to the SNMPv2 manager as SNMPv2 trap PDU
Chapter 6 SNMP Management : SNMPv2
Compatibility with SNMPv1: SNMP Proxy Server (2/2)